Chapter 9 A

1.	T

2.	F

3.	T

4.	T

5.	F

6.	T

7.	F

8.	T

9.	T

10.	B

11.	B

12.	D

13.	C

14.	D

15.	C

16.	p =  Total number of defects from all samples ( (Number of samples x sample
            size)

=   = 75/1500=0.05

Sp= where n = sample size (100)

=  + 0.0218

UCL = p + 2.17 Sp = 0.05 + 2.18(0.02) = 0.0973

LCL =  p  - 2.17 Sp = 0.05 – 2.18(0.02) = 0.0027

Plotting the fraction defectives within the control limits you determine, you’ll notice point #5 is above or outside the upper control limit and point #9 is below or outside the lower control limit.

17.      From Ex. 9A.9 on page 344 of the text, c=1, n=71.

AQL=0.005, LTPD=0.05, beta=0.010, alpha=0.005

0.05/0.005=10    C=1

0.355/0.005=71

- p-bar = 540/(20 x 500) = 540/10000 = 0.054

Sp=   = Square root of [0.054(1-0.054/500)] = 0.010

UCL = 0.054 + 2.58(0.010) = 0.080

LCL = 0.054 – 2.58(0.010) = 0.028