# Ch 7 Input and Output

Lecture Outline

## Competencies pg 176

### Define input.

### Describe keyboard entry, pointing devices, and scanning devices.

### Discuss image capturing devices, digitizing devices, and audio input devices.

### Define output.

### Describe monitors, printers, and audio output devices.

### Discuss combination input and output devices.

## Introduction pg 177

- Computer Input and output devices are essentially translators.

- Input devices translate numbers, letters and actions that people understand into a form that the computer can process.

- Output devices translate the machine language the computer can process back into letters, numbers, sounds, and images that people can understand.

- Competent end users need to know about the most common input devices such as keyboards, mice, scanners, digital cameras, digitizing tablets, voice recognition devices, and MIDI.

- They also need to know about the most common output devices such as monitors, printers, and audio output.

- They also need to know about combination input/output devices such as fax machines, Internet telephones, and terminals.

## What is Input pg 178

- Input is any data or instructions that are used by a computer.

- They can come directly from you or from other sources.

- Input devices are hardware used to translate words, sounds, images, and actions that people understand into a form that the system unit can process.

## Keyboard Entry pg 178

- Keyboards convert numbers, letters, and special characters into electronic signals.

- Most keyboards have their alphabetic characters arranged in the standard QWERTY format (note the first six characters on the top row of a keyboard).

### Keyboards

- Traditional keyboards: full-sized, rigid, rectangular keyboards that include function, navigational, and numeric keys.

- Flexible keyboards: fold or roll up for easy packing and storage for mobile users.

- Ergonomic keyboards: similar to traditional, but designed to specifically alleviate wrist strain associated with repetitive movements of typing.

- Wireless keyboards: more expensive than traditional keyboards, but give the flexibility of un-tethering the cord.

- PDA keyboards: miniature keyboards for PDAs for sending email, etc.

### Features

- Numeric keypads: easier entry of numbers and arithmetic symbols

- Toggle keys: on off keys for such things as Caps Lock and Scroll Lock

- Combination keys: perform an action when combined with other keys, e.g. <Ctrl> key or <Alt> key

## Pointing Devices pg 180

### Mouse

- A mouse controls the pointer displayed on the monitor

- The mouse pointer usually appears in the shape of an arrow

- Mechanical mouse: traditional mouse with a ball in the bottom and cord connecting it to the computer

- Optical mouse: has no moving parts – it emits and senses light to detect mouse movement.

- Cordless or wireless mouse: a battery operated device that typically uses radio waves or infrared light waves to communicate with the system.

- Other similar pointing devices include:

- Trackball (aka Roller Ball)

- Touch surfaces (aka Touch Pads)

- Pointing stick (aka Trak Point)

### Joystick

- Most popular input device for computer games

### Touch Screen

- Monitor with a touch sensitive plastic screen

- Typically used for restaurants, ATM’s and information kiosks

### Light Pen

- A light sensitive pen-like device

- Typically used for editing digital images.

## Scanning Devices pg 182

- Scanning devices convert scanned text and images into a form that the system unit can process.

### Optical Scanners

- An optical scanner (aka scanner) accepts documents consisting of text and/or images and converts them to machine readable form.

- They work be recognizing light, dark, and colored areas that make up individual letters or images.

- Flatbed scanners: work like a copy machine

- Portable scanners: typically a hand held device that slides across the document being scanned.

- Typical use is by advertising professionals who scan images and combine them with text.

### Bar Code Readers

- Bar code readers/scanners contain photoelectric cells that read bar codes.

- Typical uses are in grocery stores that use Universal Product Codes (UPC) which match up the product with a database entry containing product information such as price.

- These devices are either handheld wand readers or platform scanners.

### Character and Mark Recognition Devices

- These devices read special characters and marks.

- Three types include:

- Magnetic Ink Character Recognition (MICR): used by banks for processing checks.  Special reader/sorter machines process the checks much faster than the older manual methods

- Optical Character Recognition (OCR): use special pre-printed characters that can be read by a light source, and are still understandable by human readers.  Retail stores frequently used these types of scanners.

- Optical Mark Recognition (OMR) aka Mark Sensing: frequently used to score multiple choice tests marked by pencil on a form.

## Image Capturing Devices pg 184

- These focus on capturing just images rather than the text/image capturing by flatbed scanners.

- See Making IT work and Tim’s Toolbox for more information

### Digital Camera

- The image is captured by CCD or CMOS sensors, and stored electronically where it can be downloaded to a computer.

### Digital Video Camera

- Similar to a camcorder, only the signals are captured in digital rather than analog format.

- WebCams (Web Cameras) are inexpensive digital (video) cameras that are used for video conferencing.

## Digitizing Devices pg 185

- Digitizing devices convert a sketch or figure into machine readable code

### Graphics Tablets

- Use a special graphic surface or tablet with a stylus or pen like device to mark on it.

- Typically used by artists to draw digital images, or by engineers to create mechanical drawings.

### Digital Notepads

- Similar to Tablet PCs except users can use regular notepads and pens.  The notepad is fitted on top of an electronic notepad that senses the writing made on top.

## Audio Input Devices pg 185

- Converts sound into digital format

### Voice

- Voice Recognition Systems use a microphone for input, and a special sound card and software translates the analog signals into digital signals that can be processed and stored.

- Discrete-speed recognition systems: recognize individual words based on their sounds.  They can NOT differentiate between same-sound words (homophones) such as their, there, and they’re.

- Continuous-speech recognition systems: are able to distinguish between same-sounding words by evaluating the context.

- Dragon Systems’ NaturallySpeaking and IBM’s ViaVoice are two well know continuous-speech recognition systems.  See http://www.caere.com/ for information

### Music

- Musical Interface Digital Interface (MIDI) is a stand that allows musical instruments to connect to a computer.

- MIDI devices are specialized musical instruments that provide input in the form of encoded digital signals representing musical sounds.

- Electronic keyboards are the most commonly used MIDI devices.

## Making IT Work for You – Digital Photography pg 186-187

- This section covers the use of digital cameras, including:

- How to transfer your photos to your computer

- Touching up your images

- Sharing your pictures

## What is Output? Pg 188

- Output is processed data or information

- Typically takes the form of text, graphics, photos, or images.

- Output devices are any hardware used to provide or create output from the computer, for example monitors, printers, speakers, etc.

## Monitors pg 189

- Also known as display screens or screens

- Output is sometimes called softcopy (as opposed to printed hardcopy)

### Features

- Clarity: the quality and sharpness of a monitor; depends on:

- Resolution: measured in Pixels (Picture Elements) e.g. 1,024 x 1,280 resolution screen displays 1,310,720 pixels.  The greater the number of pixels, the better the resolution.

- Dot Pitch: the distance between pixels, typically measured in millimeters.  Most monitors have a dot pitch less than 0.3 mm.  The smaller the dot pitch, the better the clarity.

- Refresh Rate: how often the image is “re-drawn” on the monitor.  Most monitors have a refresh rate of 75 Hz or better (image refreshes 75 times every second).  The faster the rate, the better the image

- Size or Viewable Size: the diagonal length of the monitor’s viewing area.  Smaller monitors have better image quality, but it’s also smaller to view.

### Cathode-Ray Tube

- Most common type of desktop monitor.

- Uses similar technology as standard TV screens

- Advantage is they are relatively inexpensive and have a high quality image display.

- Disadvantage is they take up a lot of room

### Flat-Panel Monitor

- Also called Liquid Crystal Displays (LCDs) because of the technology that they use to display the image.

- The advantage is they take up less room, and are frequently used on laptop computers.

- Two basic types are:

- Passive matrix (dual scan monitors): lower power, but poorer clarity

- Active matrix (TFT: Thin Film Transistor): cost more, use more power, but a much better image.

### Other Monitors

- E-books (aka e-book readers) are PDA sized devices that display text and graphics.  These have not had a lot of commercial success, yet it is possible to download e-books onto computers.

- Data projectors:

- High Definition TeleVision (HDTV): a merger of microcomputers and television (PC/TV) offers much clearer and more detailed wide screen pictures than a standard TV (but currently at more cost).  Since images are digital, they can be stored and edited.

## Printers pg 191

### Features

- Resolution: measured in Dots Per Inch (DPI), typically 300, 600, or 1,200 in modern printers.  The more dots, the better the image, but the more ink that is used.  Photo printing uses even higher dpi printers (2,400 & 4,800 dpi)

- Color capability: Black & White or color

- Speed: typically measured in Pages Per Minute (ppm).  Personal printers typically print 10-15 ppm for a single color (black) and 5-10 color

- Memory: most printers have on-board RAM to buffer the print so the computer is free to do other tasks.

### Ink-Jet Printer

- Widely used technology that sprays ink onto paper.

- They are relatively inexpensive, quiet, and reliable.

### Laser Printer

- Use technology similar to a photocopier

- Cheaper printers don’t support color

- Office printers may print color, and print at high speeds

### Thermal Printer

- Not as common as Ink-Jet and Laser printers

- Used for high end artwork and image reproduction

### Other Printers

- Dot matrix printers: older technology, but good for multipart forms

- Plotters: special purpose for making maps, images, drawings

- Photo printers: special purpose for higher quality images on photo stock.

## Audio Output Devices pg 193

- Most widely used devices are speakers and headphones

- Many systems support 5.1 digital sound

## Combination Input and Output Devices pg 193

### Fax machines

- Also know as Facsimile Transmission Machines, it’s and older technology used to transmit a “picture” of a document.

### Multifunction Devices (MFD)

- These devices combine the functions of a printer, scanner, copier, and fax into one unit.

- The advantage is it can save cost over buying separate units, as well as space.

- The disadvantage is the functionality may not be as good as separate machines, and if one goes bad, you may need to replace the whole device.

### Internet Telephone

- Also known as Telephony, Internet telephony, IP telephony and Voice Over IP (VoIP) – Note: IP = Internet Protocol

- Convert analog voice into digital, and utilizes the Internet Protocol to send the digital signals.

- This technology is proving to be a popular, cost saving tool for both businesses and home users.

### Terminals

- Older technology often used to connect to a mainframe or host/server computer.

- Dumb terminals: only provide input and output to the host

- Intelligent terminals (Smart terminals) can do some processing at the terminal – an example would be a PC hooked up to act as a terminal as well.

- Network terminal (aka thin client or network computer) is a low cost alternative to an intelligent terminal.  Most don’t have storage capabilities, but are able to do some local processing.  Sun Microsystems has tried to push this model of computing for years.

- Internet terminal (aka web terminal or web appliance) is designed to provide inexpensive, easy access to the Internet.

## A Look to the Future pg 196

- Neural Signals Inc. Creates Brain-Machine Interface.

- The idea behind this product is to control a computer simply by thinking about doing it rather than physically controlling it.

- Additional material can be found at http://www.neuralsignals.com/

## Visual Summary at a glance Input and Output pg 198

### Input

#### Keyboards

#### Pointing devices

##### Mouse

##### Joysticks

##### Touch Screens

##### Light Pens

### Input

#### Scanners

##### Optical scanners

##### Bar code readers

##### Character and mark recognition devices

#### Image capturing Devices

### Input

#### Digitizing Devices

##### Graphic tablets

##### Digital notepads

#### Audio Input Devices

##### Voice recognition systems

##### Musical Instrument Digital Interface (MIDI)

### Output

#### Monitors

##### Cathode ray tubes (CRTs)

##### Flat-panel monitors (Liquid Crystal Displays – LCDs)

### Output

#### Printers

##### Ink-jet printers

##### Laser printers

##### Thermal printers

#### Audio Output Devices

### Combination Devices

#### Fax Machines

#### Multifunction Devices (MFDs)

#### Internet Telephones

#### Terminals

## Key Terms pg 201

| 1 | active-matrix monitor |  | 190 | aka TFT monitor; laptop LCD screen type with higher power consumption, but better clarity |
| --- | --- | --- | --- | --- |
| 2 | audio input device |  | 185 | microphone |
| 3 | audio input |  | 185 | a way to convert sounds into bits that the computer can process |
| 4 | audio output device |  | 193 | speakers |
| 5 | bar code |  | 183 | printed series of lines that the computer can recognize as different characters, e.g. a UPC bar code used in grocery stores |
| 6 | bar code reader |  | 183 | specialized input device to scan information such as Universal Product Codes (UPC) on grocery items |
| 7 | bar code scanner |  | 183 | specialized input device (typically handheld) to scan information such as retail price tags |
| 8 | cathode ray tube monitor | CRT | 189 | traditional, TV like picture tube offers high quality at a low price, but tends to be bulky |
| 9 | character recognition device |  | 183 | generic term used for a variety of electronic character readers such as OCR , OMR or MICR |
| 10 | Clarity |  | 189 | the quality of resolution, depends on factors such as number of pixels |
| 11 | color capability (printer) |  | 191 | the ability to print in color, typically via ink-jet or laser print technology |
| 12 | combination device |  | 193 | Acts as both input and output, e.g. FAX machine, MFD, IP phone |
| 13 | combination key |  | 179 | keys such as <Ctrl> or <Alt> that are typically used in combination with another key for executing different keyboard functions |
| 14 | continuous-speech recognition system |  | 188 | a system to convert spoken words into computer useable format, using grammar rules to help interpret the words |
| 15 | cordless mouse |  | 180 | battery operated mouse that uses wireless signals to transmit location to the computer |
| 16 | data projector |  | 190 | book sized projector for displaying computer images on a screen for presentation purposes |
| 17 | digital camera |  | 184 | camera that stores images electronically rather than on film |
| 18 | digital notepad |  | 185 | input device to allow hand written or draw images to be converted to digital format the computer can use |
| 19 | digital video camera |  | 184 | video camera that stores images in digital (computer ready) format rather than analog format |
| 20 | digitizing device |  | 185 | generic term for input equipment that converts data into digital (computer ready) format |
| 21 | discrete-speech recognition system |  | 188 | cheaper voice recognition system that only digitizes words with out taking context into consideration |
| 22 | display screen |  | 189 | generic term for any computer monitor |
| 23 | dot-matrix printer |  | 192 | older technology for printers, used small pins that would strike a ribbon to form characters |
| 24 | dot pitch |  | 189 | the space between pixels on a monitor - typically less than .30 mm |
| 25 | dots-per-inch | dpi | 191 | measurement for print quality, typically 300 x 300 up to 4800 x 4800 dpi |
| 26 | download |  | 184 | transfer a file or data from a server computer to the one you are working on |
| 27 | dual-scan monitor |  | 190 | aka passive matrix monitor, require low power and scan down the screen |
| 28 | dumb terminal |  | 195 | simple input (keyboard) output (monitor) device often used with mainframe systems |
| 29 | e-book |  | 190 | aka electronic book - the contents of which can be shown on a computer/e-book display |
| 30 | e-book reader |  | 190 | the device (separate hardware or a PC) and software that is used to display electronic books |
| 31 | facsimile machine | fax | 194 | aka FAX, essentially a low resolution picture of a document that can be transmitted electronically |
| 32 | flat-panel monitor |  | 190 | aka LCD monitor, often used with laptop computers, take up less space, but tend to be more expensive than CRT monitors |
| 33 | flatbed scanner |  | 183 | book sized unit used to digitize full sized documents |
| 34 | graphics tablet |  | 185 | input device to allow hand written or draw images to be converted to digital format the computer can use |
| 35 | hard copy |  | 191 | generic term for printed copy (permanent copy) |
| 36 | headphones |  | 193 | small speakers that can be worn by the user |
| 37 | high-definition television | HDTV | 190 | newer technology TV system offering better quality pictures |
| 38 | host computer |  | 195 | aka mainframe computer or central computer - the main server of data and applications |
| 39 | image capturing device |  | 184 | generic term for digital cameras or digital video cameras |
| 40 | ink-jet printer |  | 191 | printer technology which sprays small drops of ink onto paper to build up the image or text of a document |
| 41 | input device |  | 178 | any type of equipment used to convert information from an end user into something the computer can process |
| 42 | input |  | 178 | the process of taking end user information and digitizing it so the computer can use it |
| 43 | intelligent terminal |  | 195 | similar to a dumb terminal, yet it can do some processing without the host |
| 44 | Internet telephone |  | 194 | newer technology that allows telephones to send voice via Internet Protocol |
| 45 | Internet telephony |  | 194 | term used to describe the use of computer connectivity to make phone calls |
| 46 | Internet terminal |  | 195 | aka web terminal or web appliance, it provides a way to access the Internet using a television for output |
| 47 | IP Telephony |  | 194 | term used to describe the use of computer connectivity to make phone calls |
| 48 | joystick |  | 181 | input device for gaming |
| 49 | keyboard |  | 178 | input device to enter alphanumeric characters |
| 50 | laser printer |  | 192 | printer technology which works like a copy machine |
| 51 | light pen |  | 182 | input device for drawing images |
| 52 | liquid crystal display | LCD | 190 | output device typically used on laptops |
| 53 | magnetic-ink character recognition | MICR | 183 | input technology used for processing bank checks |
| 54 | mark recognition device |  | 183 | input technology used for reading pencil marks on a form, such as a standardized test form |
| 55 | mark sensing |  | 183 | input technology used for reading pencil marks on a form, such as a standardized test form |
| 56 | mechanical mouse |  | 180 | traditional mouse, uses a roller ball on the bottom to move sensors that pick up the location |
| 57 | memory (printer) |  | 191 | chips to temporarily store the document before it's actually printed (used to speed up the print process) |
| 58 | Musical Interface Digital Interface | MIDI | 188 | computer input for musical instruments, typically set up with a piano keyboard |
| 59 | MIDI device |  | 188 | computer input for musical instruments, typically set up with a piano keyboard |
| 60 | monitor |  | 189 | output screen for a computer, usually refers to a CRT display |
| 61 | mouse |  | 180 | input device to allow the user to "move around" on a computer screen using a GUI interface |
| 62 | mouse pad |  | 180 | smooth pad to move a mouse on |
| 63 | mouse pointer |  | 180 | the cursor for a mouse as it appears on the screen |
| 64 | multifunction device | MFD | 194 | a single unit that offers scanning, copying, printing and faxing |
| 65 | network computer |  | 195 | an low cost alternative to intelligent terminal, it provides input and output to a host server, but can do some processing |
| 66 | network terminal |  | 195 | an low cost alternative to intelligent terminal, it provides input and output to a host server, but can do some processing |
| 67 | numeric keypad |  | 178 | separate keys on a keyboard to allow fast entry of numbers |
| 68 | optical-character recognition | OCR | 183 | input technology to scan in printed characters and translate them into alphanumeric characters |
| 69 | optical-mark recognition | OMR | 183 | input technology used for reading pencil marks on a form, such as a standardized test form |
| 70 | optical mouse |  | 180 | mouse that uses light to determine location rather than a roller ball |
| 71 | optical scanner |  | 182 | generic term for devices that digitize printed documents into computer ready format |
| 72 | output |  | 188 | term used to describe the conversion of computer data into end user understandable data |
| 73 | output device |  | 188 | any equipment to present information in a form the end user can use, e.g. printers, monitors, speakers |
| 74 | passive-matrix monitor | PC/TV | 190 | aka dual scan monitor, require low power and scan down the screen |
| 75 | personal laser printer |  | 192 | lower priced (and typically lower capacity) laser printer |
| 76 | photo printer |  | 192 | specialized printer for printing photos directly from a digital camera |
| 77 | pixel (picture element) |  | 189 | unit of measure for an image or monitor - the more pixels, the higher the quality of the display |
| 78 | platform scanner |  | 183 | aka flatbed scanner, scans in and digitizes full size printed documents |
| 79 | plotter |  | 192 | output device for map making or drawings |
| 80 | pointing |  | 180 | process of giving the location of an item by gesturing |
| 81 | pointing device |  | 180 | an input device to point to an item on a screen, e.g. a mouse |
| 82 | pointing stick |  | 180 | aka trak point, a small device in the middle of a keyboard that you use like a small joystick |
| 83 | portable scanner |  | 183 | aka wand reader, it is used to get input from pre-printed forms or to read in small amounts of text |
| 84 | printer |  | 191 | output device to create hard copy or permanent copy |
| 85 | reader/sorter |  | 183 | a special machine to scan in an separate MICR encoded documents such as bank checks |
| 86 | refresh rate |  | 189 | the number of times a monitor screen is "re scanned" to display the image - typically over 70 Hz (70 x per second) |
| 87 | resolution (monitor) |  | 189 | the quality of the display, depends on pixels, refresh rate, etc. |
| 88 | resolution (printer) |  | 191 | the quality of the printer, measured in dots per inch, e.g. 300 x 300 dpi is common for lower quality print |
| 89 | roller ball |  | 180 | rubberized globe in a computer mouse that moves to activate sensors that relay position on the screen |
| 90 | scanner |  | 182 | term used to describe equipment used to read printed documents and convert them to digital data |
| 91 | scanning device |  | 182 | term used to describe equipment used to read printed documents and convert them to digital data |
| 92 | screen |  | 189 | aka monitor |
| 93 | server |  | 195 | computer which shares resources such as files, programs, printers, storage, and web pages |
| 94 | shared laser printer |  | 192 | a networked printer that several users may use |
| 95 | size (viewable size) |  | 189 | measurement for monitors, it is measured diagonally in inches, e.g. a 15 monitor may have a 13.7 inch viewable size |
| 96 | soft copy |  | 189 | term used to describe temporary output such as that from monitors and speakers |
| 97 | speakers |  | 193 | reproduce sounds from electronic signals |
| 98 | speed (printer) |  | 191 | printer speed is typically measured in ppm - pages per minute e.g. 6 ppm color 12 ppm B/W |
| 99 | telephony |  | 194 | term used to describe the use of computer connectivity to make phone calls |
| 100 | terminal |  | 195 | device used for simple input and output of computer data |
| 101 | thermal printer |  | 192 | specialized printer used for high quality images |
| 102 | thin client |  | 195 | an low cost alternative to intelligent terminal, it provides input and output to a host server, but can do some processing |
| 103 | thin film transistor monitor | TFT | 190 | aka active matrix monitor; laptop LCD screen type with higher power consumption, but better clarity |
| 104 | toggle key |  | 179 | key on a keyboard that you turn on and off, e.g. Caps Lock or Num Lock |
| 105 | touch pad |  | 180 | sensitive area on some keyboards that you can use as a mouse |
| 106 | touch screen |  | 181 | specialized monitor that you can touch to activate functions, often used on information kiosks or ATM machines |
| 107 | touch surface |  | 180 | sensitive area on some keyboards that you can use as a mouse |
| 108 | trackball |  | 180 | "upside down" mouse |
| 109 | Universal Product code | UPC | 183 | special bar code often used in the grocery industry for product pricing |
| 110 | voice recognition system |  | 185 | system used to convert spoken words into digital information |
| 111 | voice-over IP | VoIP | 194 | aka IP telephony, the use of Internet protocols to transmit phone calls |
| 112 | wand reader |  | 183 | handheld device used to scan in bar codes or optical characters |
| 113 | Web appliance |  | 195 | aka web terminal or internet terminal, it provides a way to access the Internet using a television for output |
| 114 | WebCam |  | 184 | aka Web camera; small device used to capture digital images for video conferencing via the Web |
| 115 | Web camera |  | 184 | aka Webcam; small device used to capture digital images for video conferencing via the Web |
| 116 | Web terminal |  | 195 | aka internet terminal or web appliance, it provides a way to access the Internet using a television for output |

## Chapter Review pg 202

### Crossword

#### Across

| 1 | TELEPHONY | PG 194 |
| --- | --- | --- |
| 4 | OCR | PG 183 |
| 6 | MFD | PG 194 |
| 9 | HOST | PG 195 |
| 10 | SCANNINGDEVICE | PG 182 |
| 12 | DPI | PG 192 |
| 14 | SOFTCOPY | PG 189 |
| 17 | SERVER | PG 195 |
| 18 | TFT | PG 190 |
| 19 | SCANNER | PG 182 |
| 20 | LCD | PG 190 |

#### Down

| 2 | PLOTTER | PG 192 |
| --- | --- | --- |
| 3 | OMR | PG 183 |
| 5 | MICR | PG 183 |
| 6 | MIDI | PG 188 |
| 7 | INPUT | PG 178 |
| 8 | PIXEL | PG 189 |
| 9 | HEADPHONES | PG 193 |
| 11 | INTELLIGENT | PG 195 |
| 13 | JOYSTICK | PG 181 |
| 15 | TERMINAL | PG 195 |
| 16 | HDTV | PG 190 |

### Multiple Choice

| 1 | B | Touch pad | Pg 180 |
| --- | --- | --- | --- |
| 2 | E | Optical | Pg 180 |
| 3 | D | Webcams | Pg 184 |
| 4 | D | Digital notepad | Pg 185 |
| 5 | B | MIDI | Pg 188 |
| 6 | B | E-book | Pg 190 |
| 7 | D | Plotters | Pg 192 |
| 8 | C | Audio output | Pg 193 |
| 9 | A | Multifunctional device | Pg 194 |
| 10 | D | Telephony | Pg 194 |

### Matching

| TERM | MATCH | NUMBER | HINT | PAGE |
| --- | --- | --- | --- | --- |
| thin client | S | 1 | Terminal that relies on host computer or server | 195 |
| ink jet printer | J | 2 | Printer that sprays ink at high speed onto paper | 191 |
| HDTV | H | 3 | Delivers a clearer and more detailed wide-screen picture than regular television | 190 |
| toggle | R | 4 | These keys turn a feature on or off | 179 |
| pointing stick | N | 5 | Similar to a mouse, this device is located in the middle of the keyboard | 180 |
| output | P | 6 | Processed data or information from a computer | 188 |
| CRT | A | 7 | Type of monitor built like a television set | 189 |
| digital camera | D | 8 | Similar to traditional cameras except that images are recorded digitally | 184 |
| wand reader | T | 9 | Scanners with photoelectric cells that read bar codes | 183 |
| ergonomic keyboard | L | 10 | Used to alleviate wrist strain that results from the repetitive movements of typing | 178 |
| MIDI | M | 11 | A standard that allows musical instruments to connect to the system unit | 188 |
| cordless mouse | C | 12 | Also known as a wireless mouse. | 180 |
| continuous speech recognition system | B | 13 | Voice system that is able to distinguish between same-sounding words | 188 |
| Internet Telephony | K | 14 | Uses the Internet rather than traditional communication lines to connect people via telephone | 194 |
| dumb terminal | G | 15 | Can be used to input and receive data but cannot process data. | 195 |
| host computer | I | 16 | Mainframe or other type of computer that a terminal connects to | 195 |
| digital notepad | E | 17 | Similar to a tablet PC except that it uses a regular notepad and pen | 185 |
| OMR device | O | 18 | Device that senses the presence or absence of a mark, such as a pencil mark | 183 |
| dpi | F | 19 | Measures printer resolution | 191 |
| TFT monitor | Q | 20 | Also known as an active matrix monitor | 190 |

### Open-ended

#### Describe the most common types of keyboards.

Traditional:

Flexible:

Ergonomic:

Wireless:

PDA:

See pages 178-179

#### Describe the different types of pointing devices.

Mouse (touch pad, track point/pointing stick):

Joystick:

Touch Screen:

Light Pen:

See pages 180-182

#### Describe the three categories of output devices.

Monitors:

Printers:

Audio:

Combination:

See page 188

#### Discuss the various types of monitors and printers.

Monitors: CRT and Flat-Panel, Other – see pages 189-190

Printers: Ink-Jet, Laser, Thermal, Other – see pages 191-192

#### What are combination input and output devices?  Describe four such devices.

Fax: a low resolution “picture” of a document that can be transmitted electronically

MFD: Multifunction Devices – combine a printer, scanner, copier and fax

IP Phones: Internet Protocol telephones – use the Internet to transmit messages

Terminals:

See pages 193-195

## Using Technology

### Digital Photography

- This section refers you to Making IT Work

### MSN TV

- This section directs students to learn something about MSN TV, a service that provides e-mail and web access via your television and telephone line rather than using a microcomputer.

- May want to discuss what the “target market” is for a product such as this.

## Expanding Your Knowledge

### Computing Essentials CD

### Handwriting Recognition

- Have students search the web to find applications for handwriting recognition.

- Samples might include various business uses, especially those that require mobility: package delivery & confirmation, order taking, etc.

## Building Your Portfolio

### Digital Input

- Students are asked to write a one page paper titled “Digital Input” and answer questions discussed in the text, such as a) Define digitizer, digital camera, etc.

- May recommend that students research these topics on line – look at some electronic retailer sites to learn about the costs and features of some of these items.

### Electronic Security

- Students are asked to write a one page summary about common applications of electronic monitoring; what have they seen, does it make them feel more secure, or is it an invasion of their privacy?

# Concept Checks at a glance

## Ch7 pg 179

### What is input?  What are input devices?

- Input is any data or instructions that are used by a computer.  They come from an end user, and must be translated into digital codes that the computer can process.

- Input devices are hardware used to translate words, sounds, images, and actions that end users produce into a digital format the computer can process.

- Examples of input devices include keyboards, a mouse, a microphone, etc.

### Discuss five common types of keyboard designs.

- Traditional keyboards: full-sized, rigid, rectangular keyboards that include function, navigational, and numeric keys.

- Flexible keyboards: fold or roll up for easy packing and storage for mobile users.

- Ergonomic keyboards: similar to traditional, but designed to specifically alleviate wrist strain associated with repetitive movements of typing.

- Wireless keyboards: more expensive than traditional keyboards, but give the flexibility of un-tethering the cord.

- PDA keyboards: miniature keyboards for PDAs for sending email, etc

### What are some common keyboard features?

- Numeric keypads: easier entry of numbers and arithmetic symbols

- Toggle keys: on off keys for such things as Caps Lock and Scroll Lock

- Combination keys: perform an action when combined with other keys, e.g. <Ctrl> key or <Alt> key

## Ch 7 pg 182

### What is a pointing device?  Discuss four pointing devices.

- A pointing device provides a comfortable interface with the system unit, by accepting pointing gestures and converting them into machine-readable input.

- Four types include:

#### Mouse

- A mouse controls the pointer displayed on the monitor

- The mouse pointer usually appears in the shape of an arrow

- Mechanical mouse: traditional mouse with a ball in the bottom and cord connecting it to the computer

- Optical mouse: has no moving parts – it emits and senses light to detect mouse movement.

- Cordless or wireless mouse: a battery operated device that typically uses radio waves or infrared light waves to communicate with the system.

- Other similar pointing devices include:

- Trackball (aka Roller Ball)

- Touch surfaces (aka Touch Pads)

- Pointing stick (aka Trak Point)

#### Joystick

- Most popular input device for computer games

#### Touch Screen

- Monitor with a touch sensitive plastic screen

- Typically used for restaurants, ATM’s and information kiosks

#### Light Pen

- A light sensitive pen-like device

- Typically used for editing digital images.

- They can include both wired and wireless technologies

### Describe the three basic mouse designs.

- Mechanical mouse: traditional mouse with a ball in the bottom and cord connecting it to the computer

- Optical mouse: has no moving parts – it emits and senses light to detect mouse movement.

- Cordless or wireless mouse: a battery operated device that typically uses radio waves or infrared light waves to communicate with the system.

- Other similar pointing devices include:

- Trackball (aka Roller Ball)

- Touch surfaces (aka Touch Pads)

- Pointing stick (aka Trak Point)

## Ch 7 pg 183

### How are pointing and scanning devices different?

- A pointing device just changes your location on the screen (moves the cursor).  A scanning device converts printed output into digital input for processing by the computer.

### Describe three types of scanners.

- Scanning devices convert scanned text and images into a form that the system unit can process.

#### Optical Scanners

- An optical scanner (aka scanner) accepts documents consisting of text and/or images and converts them to machine readable form.

- They work be recognizing light, dark, and colored areas that make up individual letters or images.

- Flatbed scanners: work like a copy machine

- Portable scanners: typically a hand held device that slides across the document being scanned.

- Typical use is by advertising professionals who scan images and combine them with text.

#### Bar Code Readers

- Bar code readers/scanners contain photoelectric cells that read bar codes.

- Typical uses are in grocery stores that use Universal Product Codes (UPC) which match up the product with a database entry containing product information such as price.

- These devices are either handheld wand readers or platform scanners.

#### Character and Mark Recognition Devices

- These devices read special characters and marks.

- Three types include:

- Magnetic Ink Character Recognition (MICR): used by banks for processing checks.  Special reader/sorter machines process the checks much faster than the older manual methods

- Optical Character Recognition (OCR): use special pre-printed characters that can be read by a light source, and are still understandable by human readers.  Retail stores frequently used these types of scanners.

- Optical Mark Recognition (OMR) aka Mark Sensing: frequently used to score multiple choice tests marked by pencil on a form.

### Describe three common character and mark recognition devices.

- Magnetic Ink Character Recognition (MICR): used by banks for processing checks.  Special reader/sorter machines process the checks much faster than the older manual methods

- Optical Character Recognition (OCR): use special pre-printed characters that can be read by a light source, and are still understandable by human readers.  Retail stores frequently used these types of scanners.

- Optical Mark Recognition (OMR) aka Mark Sensing: frequently used to score multiple choice tests marked by pencil on a form.

## Ch 7 pg 188

### What is the difference between scanning and image capturing?

- Scanning focuses on converting printed text into machine readable codes

- Image capturing converts photos and moving pictures into digital format.

### How are digital cameras different from traditional cameras?

- Digital cameras store the images electronically

- Traditional cameras use film

### What are digitizing devices?

- Digitizing devices convert a sketch or figure into machine readable code

#### Graphics Tablets

- Use a special graphic surface or tablet with a stylus or pen like device to mark on it.

- Typically used by artists to draw digital images, or by engineers to create mechanical drawings.

#### Digital Notepads

- Similar to Tablet PCs except users can use regular notepads and pens.  The notepad is fitted on top of an electronic notepad that senses the writing made on top.

### Describe voice recognition systems.  What is MIDI?

#### Voice recognition systems

- Voice Recognition Systems use a microphone for input, and a special sound card and software translates the analog signals into digital signals that can be processed and stored.

- Discrete-speed recognition systems: recognize individual words based on their sounds.  They can NOT differentiate between same-sound words (homophones) such as their, there, and they’re.

- Continuous-speech recognition systems: are able to distinguish between same-sounding words by evaluating the context.

- Dragon Systems’ NaturallySpeaking and IBM’s ViaVoice are two well know continuous-speech recognition systems.  See http://www.caere.com/ for information

#### MIDI

- Musical Interface Digital Interface (MIDI) is a stand that allows musical instruments to connect to a computer.

## Ch 7 pg 191

### What is output?  What are output devices?

- Output is processed data or information

- It typically takes the form of text, graphics, photos, audio, or video

- Output devices are any hardware used to provide or create output from the computer, e.g. printers, monitors, speakers, etc.

### Define these monitor features: resolution, dot pitch, refresh rate, and size.

- Clarity: the quality and sharpness of a monitor; depends on:

- Resolution: measured in Pixels (Picture Elements) e.g. 1,024 x 1,280 resolution screen displays 1,310,720 pixels.  The greater the number of pixels, the better the resolution.

- Dot Pitch: the distance between pixels, typically measured in millimeters.  Most monitors have a dot pitch less than 0.3 mm.  The smaller the dot pitch, the better the clarity.

- Refresh Rate: how often the image is “re-drawn” on the monitor.  Most monitors have a refresh rate of 75 Hz or better (image refreshes 75 times every second).  The faster the rate, the better the image

- Size or Viewable Size: the diagonal length of the monitor’s viewing area.  Smaller monitors have better image quality, but it’s also smaller to view

### Describe CRTs, flat-panel, and specialty monitors.

- Distributed processing separates the data processing onto different servers rather than on one dedicated host computer

#### Cathode-Ray Tube

- Most common type of desktop monitor.

- Uses similar technology as standard TV screens

- Advantage is they are relatively inexpensive and have a high quality image display.

- Disadvantage is they take up a lot of room

#### Flat-Panel Monitor

- Also called Liquid Crystal Displays (LCDs) because of the technology that they use to display the image.

- The advantage is they take up less room, and are frequently used on laptop computers.

- Two basic types are:

- Passive matrix (dual scan monitors): lower power, but poorer clarity

- Active matrix (TFT: Thin Film Transistor): cost more, use more power, but a much better image.

#### Other (Specialty) Monitors

- E-books (aka e-book readers) are PDA sized devices that display text and graphics.  These have not had a lot of commercial success, yet it is possible to download e-books onto computers.

- Data projectors:

- High Definition TeleVision (HDTV): a merger of microcomputers and television (PC/TV) offers much clearer and more detailed wide screen pictures than a standard TV (but currently at more cost).  Since images are digital, they can be stored and edited.

## Ch 7 pg 192

### Discuss the printer features: resolution, color capability, speed, and memory

- Resolution: measured in Dots Per Inch (DPI), typically 300, 600, or 1,200 in modern printers.  The more dots, the better the image, but the more ink that is used.  Photo printing uses even higher dpi printers (2,400 & 4,800 dpi)

- Color capability: Black & White or color

- Speed: typically measured in Pages Per Minute (ppm).  Personal printers typically print 10-15 ppm for a single color (black) and 5-10 color

- Memory: most printers have on-board RAM to buffer the print so the computer is free to do other tasks

### Discuss three types of commonly used printers

#### Ink-Jet Printer

- Widely used technology that sprays ink onto paper.

- They are relatively inexpensive, quiet, and reliable.

#### Laser Printer

- Use technology similar to a photocopier

- Cheaper printers don’t support color

- Office printers may print color, and print at high speeds

#### Thermal Printer

- Not as common as Ink-Jet and Laser printers

- Used for high end artwork and image reproduction

### Discuss dot-matrix, plotter, and photo printers

- Dot matrix printers: older technology, but good for multipart forms

- Plotters: special purpose for making maps, images, drawings

- Photo printers: special purpose for higher quality images on photo stock

## Ch 7 pg 195

### What are the two most widely used audio output devices?

- Most widely used devices are speakers and headphones

- Many systems support 5.1 digital sound

### What are combination input and output devices?

- Equipment that act as both input and output, e.g. a FAX machine, MFD, IP phone, etc.

### Describe the following combination devices: fax machine, MFD, Internet telephone, and terminal.

#### Fax machines

- Also know as Facsimile Transmission Machines, it’s and older technology used to transmit a “picture” of a document.

#### Multifunction Devices (MFD)

- These devices combine the functions of a printer, scanner, copier, and fax into one unit.

- The advantage is it can save cost over buying separate units, as well as space.

- The disadvantage is the functionality may not be as good as separate machines, and if one goes bad, you may need to replace the whole device.

#### Internet Telephone

- Also known as Telephony, Internet telephony, IP telephony and Voice Over IP (VoIP) – Note: IP = Internet Protocol

- Convert analog voice into digital, and utilizes the Internet Protocol to send the digital signals.

- This technology is proving to be a popular, cost saving tool for both businesses and home users.

#### Terminals

- Older technology often used to connect to a mainframe or host/server computer.

- Dumb terminals: only provide input and output to the host

- Intelligent terminals (Smart terminals) can do some processing at the terminal – an example would be a PC hooked up to act as a terminal as well.

- Network terminal (aka thin client or network computer) is a low cost alternative to an intelligent terminal.  Most don’t have storage capabilities, but are able to do some local processing.  Sun Microsystems has tried to push this model of computing for years.

- Internet terminal (aka web terminal or web appliance) is designed to provide inexpensive, easy access to the Internet.

- Common network strategies are terminal, client server, and peer-to-peer systems

# List of Figures at a glance

- Ch 7 pg 178 figure 7-1 Flexible keyboard

  - Photo of a flexible keyboard, somewhat “untraditional” but may be useful for its portability

- Ch 7 pg 179 figure 7-2 Ergonomic keyboard

  - Photo of a curved, ergonomic keyboard designed to alleviate wrist strain associated with the repetitive movements of typing

- Ch 7 pg 179 figure 7-3 PDA with keyboard

  - Photo of a Palm PDA with a small keyboard built into the device for simple data input

- Ch 7 pg 179 figure 7-4 Traditional keyboard

  - Image of a traditional 101-key keyboard with some of the special keys highlighted including:

    - The Escape key

    - Function keys

    - Numeric keypad

    - Windows key

    - Spacebar

    - Navigation (arrow) keys

- Ch 7 pg 180 figure 7-5 Standard mouse: along with some key features including:

  - Left button

  - Right button

  - Retaining ring

  - Mouse cable

  - Roller ball

- Ch 7 pg 181 figure 7-6 Optical mouse

  - Photo of the top and bottom side of an optical mouse which uses light to determine the motion rather than a roller ball touching sensors

- Ch 7 pg 181 figure 7-7 Touch surface

  - Photo of a person using a “track pad” as a pointing device

- Ch 7 pg 181 figure 7-8 Joystick

  - Photo of a “game” joystick

- Ch 7 pg 181 figure 7-9 Touch screen

  - Photo of a woman using a touch screen on an information kiosk

- Ch 7 pg 182 figure 7-10 A Light pen

  - Image of a light pen on a digitizing surface for creating and editing a digital image

- Ch 7 pg 182 figure 7-11 Two types of scanners

  - A flatbed scanner used to digitize full size paper documents

  - A portable scanner used to digitize a few words at a time

- Ch 7 pg 183 figure 7-12 Bar code reader

  - Photo of a grocery store Universal Product Code (UPC) bar code on a carton of milk being scanned

- Ch 7 pg 183 figure 7-13 Wand reader

  - Photo of a woman using a wand reader to scan in a price code of some clothing

- Ch 7 pg 184 figure 7-14 Digital camera

  - Photo of a boy using a digital camera to take a picture

  - Digital cameras store the image electronically rather than on film

- Ch 7 pg 184 figure 7-15 WebCam

  - Photo of a woman using a WebCam to conduct a video conference via the Internet.  The camera will display her image on another computer.

- Ch 7 pg 185 figure 7-16 Graphics tablet

  - Photo of person using a graphics tablet to input handwriting or drawing into a computer

- Ch 7 pg 185 figure 7-17 Portable voice recognition system

  - Photo of an Olympus voice recording device that will digitize a human voice for use on a computer

- Ch 7 pg 188 On the Web Explorations

  - This section encourages students to research Dragon Soft, a leader in voice recognition software (continuous speech recognition systems)

- Ch 7 pg 189 figure 7-18 Monitor resolution

  - Blow up image showing pixels (picture elements) on a monitor

  - Resolution is affected by

    - Number of pixels

    - Dot pitch (space between pixels)

    - Refresh rate

    - And the viewable size of the monitor

- Ch 7 pg 189 figure 7-19 Resolution standards

  - Table of common resolution standards including:

    - SVGA 800 x 600 pixels

    - XGA 1,024 x 768

    - SXGA 1,280 x 1,024

    - UXGA 1,600 x 1,200

- Ch 7 pg 189 figure 7-20 CRT monitor

  - CRT – Cathode Ray Tube is a “traditional monitor” similar to a standard television screen

  - The offer great clarity, and are fairly inexpensive, but bulky

- Ch 7 pg 190 figure 7-21 Flat-panel monitor

  - Flat panel monitors or LCD (Liquid Crystal Displays) monitors offer quality output, but tend to cost more.  They also take up much less space

- Ch 7 pg 190 figure 7-22 E-book

  - E-books – Electronic books – were marketed to offer a low cost solution for reading electronic copies of books.

- Ch 7 pg 190 figure 7-23 Data projector

  - Typically used to project PowerPoint or other computer images to a large group during a presentation

- Ch 7 pg 191 On the Web Explorations

  - Students are encouraged to learn more about HDTV (High Definition TV)

- Ch 7 pg 191 figure 7-24 A special application ink-jet printer

  - Image showing a man printing a large high quality poster using a specialized ink-jet printer

- Ch 7 pg 192 TIPS box

  - This section offers tips for saving paper when you print from the Web including:

    - Preview

    - Choose Printer Friendly

    - Print Selection

- Ch 7 pg 193 figure 7-25 Photo printer

  - A specialized printer to print a photograph directly from a digital camera

- Ch 7 pg 193 figure 7-26 Headphones

  - Photo of a man listening to headphones attached to his computer

- Ch 7 pg 194 figure 7-27 Internet telephone

  - Internet telephones transfer voice via Internet Protocols rather than over standard phone protocols, potentially saving the user money

- Ch 7 pg 195 figure 7-28 Dumb terminals are used for airline reservations

  - Photo showing an airline reservation terminal in use