Chapter 12, Printers

# |1|	Chapter Overview

## A.	Printer basics

## B.	Printer ports

## C.	Dot-matrix printers

## Ink-jet printers

## E.	Laser printers

Chapter 12, Lesson 1

Printers

# |2|	1.	Printer Basics

## A.	Printer evaluation issues

### 1.	Printer resolution is measured in dots per inch (dpi).

### 2.	Speed is measured in the number of plain-text pages (with 5 percent coverage) per minute.

### 3.	To print graphics, the printer must support a printer language such as PostScript or Printer Control Language (PCL).

### 4.	Paper capacity includes the number and type of paper trays, number of sheets per tray, and size of sheets.

### 5.	Duty cycle is measured in number of plain-text pages (with 5 percent coverage) the printer is rated to print per month.

### 6.	Complex graphics and full-color images require more memory than plain-text pages.

### 7.	Cost of paper: special paper is sometimes required, such as for photo quality images or ink-jet printers (to avoid smearing and distorting).

### 8.	Cost of consumables: cost per page, including cost of replacement ink or toner cartridge

## |3|	B.	Common printer terms

### 1.	American Standard Code for Information Interchange (ASCII) is the standard code for representing characters as numbers.

### 2.	A font is a collection of characters and numbers in a given size, expressed in style name and size, for example, Times New Roman, 11 points (pts).

### 3.	The line print terminal (LPT) port is a standard parallel printer port on a computer.

### 4.	Laser Jet PCL

#### a.	Hewlett-Packard’s printer control language

#### b.	Contents of the page are described as bitmapped pixels on the page.

### 5.	Adobe PostScript

#### a.	The most common page-description language (PDL)

#### b.	Contents of the page are described as scalable elements.

#### c.	A PostScript interpreter in the printer makes the conversion from scale to bitmap at print time.

### 6.	Resolution enhancement is a technology that improves the appearance of images and other forms of graphics by modifying tonal ranges, improving halftone placement, and smoothing the jagged edges of curves.

### 7.	Printing orientation

#### a.	Portrait: the vertical orientation of printing on a page

#### b.	Landscape: the horizontal orientation of printing on a page

### 8.	Duplexing: the ability to print on both sides of a page

# |4|	2.	Printer Ports

## A.	Ports can be serial, Small Computer System Interface (SCSI), or parallel, although parallel is the most common.

## B.	The parallel port consists of a 25-pin male plug.

## Parallel ports are relatively trouble free but have some disadvantages.

### 1.	The data transfer rate is 150 KB per second—slow compared to network cards and other high-speed interfaces.

### 2.	Rely on system bus and CPU for transport and management, which uses system resources while printing

### 3.	Although parallel ports and cable follow common practices, there are no standards.

### 4.	Parallel cables have a maximum effective length of 10 feet, although this length can be extended with a booster device.

# |5|	3.	Dot-Matrix Printers

## A.	An impact printer creates an impression on the page by striking an ink ribbon with force to place ink on the page.

## B.	Very common before the advent of ink-jet and laser technology printers

## C.	Still used to print multipart forms, especially in business offices that need the ability to print several copies at once

## D.	Use either 9 or 24 pins to render an image. The 24-pin printers generate a higher-quality image.

## |6|	E.	Maintaining a dot-matrix printer

### 1.	Change the ribbon.

### 2.	Keep the printer clean.

### 3.	Keep the print head clean.

### 4.	Replace the print head if it fails.

## |7|	F.	Troubleshooting dot-matrix printers

### 1.	Printer does not print: the printer has no power, is offline, out of paper, or the printer cable is disconnected

### 2.	Paper/Error indicator flashes continuously: this indicates an overload condition

### 3.	Paper slips around platen: the paper-feed selector needs to be adjusted

### 4.	Paper bunches up: there is no reverse tension

### 5.	Paper has dimples: the paper is misaligned or the tractor feed wheels are not locked

### 6. 	Print mode cannot be set: the printer configuration switch is improperly set

# |8|	4.	Ink-Jet Printers

## A.	Spray ink onto paper to form images

## B.	Provide good-quality, reasonably fast printing

## C.	Produce color as well as black-and-white images

## D.	Have replaced dot-matrix and thermal wax printers in the low-end market

## |9|	E.	Maintaining an ink-jet printer

### 1.	Keep the printer clean.

### 2.	Replace ink cartridges as needed.

#### a.	Follow the instructions carefully.

#### b.	The cartridge must be properly pressurized.

#### c.	Sensors must line up with contacts on the cartridge transport.

## |10|	F.	Troubleshooting ink-jet printers

### 1.	Inspect the printer for obvious problems such as a paper jam or empty paper tray.

#### a.	Most printers have a light-emitting diode (LED) panel to signal problems.

### 2.	Use the printer self-test routine.

### 3.	Common symptoms and possible causes

#### a.	The printer does not print: the printer has no power, is offline, out of paper, or the printer cable is disconnected

#### b.	Printer will not go online: check the cartridge and printer cable

#### c.	All lights off: check the power supply fuse and check for signs of binding

#### d.	Print head does not print: check the ink supply

#### e.	Paper does not advance: the paper-handling hardware is jammed

# |11|	5.	Laser Printers

## A.	Nonimpact devices that precisely place a fine plastic powder (toner) on paper

## B.	Range from personal, lower-volume, desktop devices to huge devices serving hundreds of users

## C.	All follow a common engine design, similar to office copiers.

## D.	More expensive to purchase than ink-jet printers

## E.	Cheaper to operate per page than ink-jet printers

## F.	Toner is more permanent than ink.

# |12|	6.	Laser Printer Components

## A.	The paper transport ranges from a straight transport to a complicated transport for duplexers, collators, and staplers.

## B.	Logic circuits: motherboard much like that of a PC

## C.	User interface: simple to advanced LED panels

## D.	Toner and toner cartridges: disposable cartridges containing toner

## E.	Photosensitive drum

### 1.	Aluminum cylinder coated with a photosensitive compound and electrically charged

### 2.	Captures the image to be printed

### 3.	Attracts the toner to be placed on the page

### 4.	Keep the drum clean and do not expose it to light unnecessarily.

## F.	A laser beam paints the printed page on the drum.

## G.	The primary corona charges the photosensitive particles on the surface of the drum.

## H.	The transfer corona charges the surface of the paper before it reaches the toner area.

## I.	Fuser rollers: a heated roller and an opposing pressure roller fuse the toner onto the paper.

## J.	The erase lamp bathes the drum in light to neutralize the electrical charge on the drum between printing pages.

## K.	Power supply: laser printers use very high power, so they should not be attached to an uninterruptible power supply (UPS).

## L.	Drivers and software: laser printers ship with drivers, diagnostic programs, and programs that allow full control of all options and real-time status reporting.

# |13|	7.	The Mechanics of Laser Printing

## Computer-to-printer communication

### 1.	The operating system sends a request to the printer.

### 2.	The printer informs the operating system that it is online and ready to accept data.

### 3.	The PC starts sending data.

### 4.	If the printer can handle bidirectional communications, the printer informs the computer of any problems encountered, such as an out-of-paper condition, paper jam, or low toner.

### 5.	After the job is complete, the printer acknowledges the receipt of all data.

## |14|	B.	The laser printing process

### 1.	The drum is cleaned.

### 2.	An image is converted into a series of raster lines and stored in memory.

### 3.	The paper is fed and the primary corona charges the drum.

### 4.	The image is set in raster lines on the drum, using positive charges.

### 5.	Toner is transferred to the positively charged areas of the drum.

### 6.	Toner is transferred from the drum to the paper, forming the image.

### 7.	The image is fused to paper and sent to the output tray.

## |15|	C.	Laser printer resolution

### 1.	The quality of a laser printer is directly related to resolution, which is measured in dpi.

### 2.	Horizontal resolution is determined by how fine a line can be drawn.

### 3.	Vertical resolution is the increment by which the drum is turned for each pass of the raster line.

### 4.	Generally, vertical and horizontal resolution are equal, such as 600 or 1200 dpi.

### 5.	Draft mode prints at lower resolution to save toner.

## |16|	D.	Troubleshooting laser printers

### 1.	Ghost (unwanted) images: the drum is not fully discharged or fully charged, or the drum is damaged

### 2.	Page prints black: the primary corona, laser scanning module, or main central board has failed

### 3.	Streaks or random spots appear: the drum was improperly cleaned

### 4.	Marks appear on every page: the drum is damaged

### 5.	Printing too light: the toner supply is low

### 6.	Memory overflow error: there is insufficient memory for print resolution

### 7.	Characters incomplete: the print density is incorrect

### 8.	Mass of melted plastic is spit out: the wrong transparency material was used

### 9.	Pages are creased: the type of paper used is not suitable

### 10.	Characters are warped, overprinted or poorly formed: there is a problem with the paper or other media or the hardware

### 11.	Paper jam indicator remains on after paper jam is cleared: the printer has not reset

### 12.	Paper continues to jam: there is a problem with the pickup area, turning area, or registration alignment area

## |17|	E.	Hardware problems

### 1.	Most laser printers allow you to print diagnostic and configuration information.

### 2.	Check for

#### a.	Status lights

#### b.	Menu warnings

#### c.	Error messages

### 3.	Use the manual to determine the steps to take in troubleshooting problems indicated by printer display.

# |18|	Chapter Summary

## A.	Dot-matrix printers are still used for printing multiple copies at once.

## B.	Ink-jet printers provide good quality at an inexpensive price.

## C.	Laser printers are more expensive initially, but cheaper per page.

## D.	Most printer problems can be resolved quickly by checking for incorrect connections, correcting improper use, or fixing paper jams.

## E.	Key components of a laser printer are the photosensitive drum, erase lamp, primary corona, laser beam, transfer corona, and fuser rollers.