Midterm                        1 Hour, 50 minutes

Do any 10 of the 12 problems.  Make sure it is clear which one you do not want graded (or I will grade the first 10 problems).  All problems are worth 20 points.

1.  The following function is already in minimum sum of products form.  Show the equation and a block diagram for an implementation using only 2-input NAND gates.  No gate may be used as a NOT.  All variables are available both uncomplemented and complemented.  For full credit, find a solution using 14 gates; partial credit for more gates or one or two

3-input gates.  Bonus of up to 5 points for less.

F  =  A' B' C' D'  +  B' C D' E  +  B D  +  B C' E'  +  C D E'  +  C' D E

2.  Show an algebraic expression for the following circuit.  Reduce it to a minimum sum of products expression (2 terms, 4 literals.)

3.  Convert the following to a sum of minterms.  Remove any duplicates from the list.

f  =  (a + b' + c) (a + c + d) (b + c') (b' + d')

4.  For the following function, find THE minimum sum of products solution.

5.  For the following function, list all of the prime implicants and find BOTH minimum sum of product expressions.  (extra maps shown for your convenience)

h (w, x, y, z)  =  ∑ m (2, 3, 5, 6, 7, 9, 10, 11, 13, 14)

6.  For the function, g, shown, show the equations and a block diagram for a minimum cost two-level NAND implementation a minimum two-level NOR implementation (spare map shown).  All variables are available both uncomplemented and complemented.

7.  For the function, F,  shown find a minimum sum of products expression and a minimum product of sums expression (spare map shown).

8.  For the following function (3 copies of the map shown), find all 4 minimum sum of products expressions.

9.  For the following 5-variable function, F, find BOTH minimum sum of product solutions.  (Two copies of the map are shown.)

10.  For the following 5-variable function, F, find the minimum sum of product solution.  (Two copies of the map are shown.)  (6 terms, 20 literals)

11.  For the two functions shown,  find a minimum two-level solution (map and equations) corresponding to 5 AND gates and 2 OR gates with a total of 19 inputs.  All inputs are available both uncomplemented and complemented.  (Show only the maps and equations.)

12.   For the three functions shown,  find a minimum two-level solution (map and equations) corresponding to 7 AND gates and 3 OR gates with a total of 30 inputs.  All inputs are available both uncomplemented and complemented.  (Show the maps and equations.)