# Quiz 1 solution			 	50 minutes

All problems worth 10 points.

1.  Convert the decimal number 311 to binary.  Show your work.

311/2  =  155	rem 1							1

155/2  =  77	rem 1							11

77/2  =  38		rem 1							111

38/2  =  19		rem 0						0111

19/2  =  9		rem 1					10111

9  =  1001							100110111

2.  Show the decimal equivalent of each of the numbers if they are interpeted as (six answers)

0 1 1 0  0 1 1 1		 1 0 0 1  0 1 0 1

a)  Unsigned binary			103				149

b)  Signed binary				+103		Magnitude: 01101011

-107

c)  BCD (8421 code)			67				95

3.  Add the two pairs of positive binary numbers.   (Be sure to show the carry as you add.)

1 1 1 1				1 0 0 0

0 1 0 1 1	11			0 1 0 1 0	10

1 0 1 1 0	22			0 1 0 0 1	  9

1	0 0 0 0 1	  1		   0	1 0 0 1 1	19

overflow

Show both operands and the result of each addition in decimal as well as binary, indicating when there is overflow.

4.  Complete the truth table for a system with 4 inputs, a, b, c, and d and one output, f.  The first three inputs (a, b, c) represent a binary number, n, in the range 0 to 7; however, the input 0 never occurs.  The last input (d) specifies which of two computations is made.

d = 0:  f is 1  iff n is a multiple of 3

d = 1:  f is 1  iff n is a multiple of 2

|  | a | b | c | d | f |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | 0 | 0 | 0 | 0 | X |  |  |
|  | 0 | 0 | 0 | 1 | X |  |  |
|  | 0 | 0 | 1 | 0 | 0 |  |  |
|  | 0 | 0 | 1 | 1 | 0 |  |  |
|  | 0 | 1 | 0 | 0 | 0 |  |  |
|  | 0 | 1 | 0 | 1 | 1 |  |  |
|  | 0 | 1 | 1 | 0 | 1 |  |  |
|  | 0 | 1 | 1 | 1 | 0 |  |  |
|  | 1 | 0 | 0 | 0 | 0 |  |  |
|  | 1 | 0 | 0 | 1 | 1 |  |  |
|  | 1 | 0 | 1 | 0 | 0 |  |  |
|  | 1 | 0 | 1 | 1 | 0 |  |  |
|  | 1 | 1 | 0 | 0 | 1 |  |  |
|  | 1 | 1 | 0 | 1 | 1 |  |  |
|  | 1 | 1 | 1 | 0 | 0 |  |  |
|  | 1 | 1 | 1 | 1 | 0 |  |  |

5.  Use a truth table to show if g1  =  g2, where

g1  =  x' z'  +  y z

g2  =  (x' + z) (y + z')

|  | x | y | z | x' z' | y z | g1 | x' + z | y + z' | g2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 |
|  | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 |
|  | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 1 |
|  | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 |
|  | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 |
|  | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 |
|  | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 |
|  | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 |

Truth tables are the same; they are equal

6.  Reduce the expression below (using the algebraic properties) to a sum of products expression with 2 terms and 4 literals.  Show each step.

a' b' c'  +  a' b' c  +  a b c  +  a b' c

=  a' b' (c' + c)  +  a c (b + b')

=  a' b 1  +  a c 1

=  a' b  +  a c

7.  Reduce the expression below (using the algebraic properties) to a sum of products expression with 3 terms and 5 literals.  Show each step.

x' y' z'  +  x' y' z  +  x' y z  +  x y' z  +  x y z  +  x y z'

=  x' y'  +  x' y z  +  x y' z  +  x y

=  x' (y' + y z)  +  x (y + y' z)

=  x' y'  +  x' z  +  x y  +  x z

=  z  +  x' y'  +  x y

or 		=  z (x' y'  +  x' y  +  x y'  +  x z)  +  x' y' z'  +  x y z'

=  z  +  x' y' z'  +  x y z'

=  z  +  z' (x' y'  +  x y)

=  z  +  x' y'  +  x y

8.  Map the following function, circling each of the terms.

f  =  a' b' c'  +  a' b  +  a b d  +  a b' c' d'

9.  Consider the following function

g  =  a b  +  b c'  +  a c'

All inputs are available both uncomplemented and complemented.

a)  Show a block diagram for a two-level AND-OR implementation.

b)  Show a block diagram for an implementation that uses only two-input AND and OR gates.

g  =  b (a + c')  +  a c'      or    g  =  c' (a + b)  +  a b

10.   For the following truth table

|  | x | y | z | f |
| --- | --- | --- | --- | --- |
|  | 0 | 0 | 0 | 1 |
|  | 0 | 0 | 1 | 0 |
|  | 0 | 1 | 0 | 1 |
|  | 0 | 1 | 1 | 1 |
|  | 1 | 0 | 0 | 0 |
|  | 1 | 0 | 1 | 0 |
|  | 1 | 1 | 0 | 0 |
|  | 1 | 1 | 1 | 1 |

a)  Write a sum of minterms function in numeric form (for example,

∑ m (0, ...)

f (x, y, z)  =  ∑ m (0, 2, 3, 7)

b)  Write a sum of minterms function in algebraic form (for example,

x' y + ...)

f  =  x' y' z'  +  x' y z'  +  x' y z  +  x y z

c)  Find a minimum sum of products expression (2 terms, 4 literals)

f  =  x' z' (y' + y)  +  y z (x' + x)

=  x' z'  +  y z