Chapter 11 FE EXAM FORMATTED PROBLEMS

11-1.	A field test of a clay liner resulted in the data shown below. Estimate the hydraulic conductivity of the liner.

Thickness of the clay line=0.60m

Clay porosity= 0.55

Breakthrough time = 90.0d

Depth of leachate above the liner = 3.0m

Solve using Eq. 11-12.

11-2.	Estimate the percent of landfill gas that is methane for a rapidly decomposing waste with the following composition: C68H111O50N, assume the maximum theoretical landfill gas may be estimated using Eq. 11-9.

11-3.	Solid waste with the density of 110 kg/m3 is spread in a 0.5m layer at a landfill. If a steel wheeled compactor can achieve a density of 400 kg/m3, what thickness of waste will be achieved?

11-4.	Estimate the weekly volume of solid waste being delivered to a municipal landfill if the average solid waste generation rate is 2.6 kg/person∙d. The population is 17,200 and the density as delivered is 122kg/m3.