Chapter 12 FE EXAM FORMATTED PROBLEMS

12-1. 	Calculate the incinerator destruction and removal efficiency for methylene chloride using the following measurements:

Aqueous influent				Stack gas effluent

Flow rate = 53.0 L/min			Flow rate = 606.5 m3/min

Concentration = 7,120 mg/L			Concentration = 188.3 μg/m3

Solve the mass flow rate for the aqueous feed and the stack gas

12-2.	What is the combustion efficiency of a PCB incinerator is the stack effluent concentration of CO =100 ppm and the concentration of CO2= 100,000 ppm?

Solve using Eq. 12-11

12-3.	If the pH controller for feeding hydroxide to a zinc precipitation tank is set at pH=8.4, what will the effluent concentration of zinc be after settling of the precipitate? The Ksp of Zn(OH)2 is 7.68x10-17.

Using precipitation Eqs. From Chapter 5

Ksp= [Zn2+][OH-]2

pOH = 14- pH = 14 – 8.4 = 5.60

[OH-]= 10-5.60 = 2.5119x10-6moles/L

12-4.	Estimate the soil partition coefficient of benzene for a soil having the following properties: bulk density = 1.4 g/cm3, porosity = 0.40, organic carbon fraction = 0.002, and retardation coefficient = 1.2.

Solve using Eq. 12-13