Chapter 4 FE EXAM FORMATTED PROBLEMS

4-1.	Lake Mead has a mean surface area of 124,200 acres and a mean annual evaporation of 849,000 acre-ft.  If the New York City water supply requires 1.53 x 109 gallons per day, how many days supply would the Lake Mead evaporation fulfill?

Converting acre-ft to gallons

Solving

4-2.	If a steady rain of 0.33 in/h falls on a parking lot with an area of 65,340 ft2 and a runoff coefficient of 0.85, what is the estimated peak discharge?

Converting square feet to acres

Solving using Eq. 4-19

4-3.	Water is pumped at a rate of 33.42 ft3/min from an unconfined aquifer that is 75ft deep.  Wells located at 100 and 150 ft from the pumping well have drawdowns of 9 and 7 ft respectively. What is the hydraulic conductivity of the soil? (Note: the FE manual uses permeability rather than hydraulic conductivity.)

Solving using Eq. 4-35

4-4.	What is the seepage velocity of water in an aquifer with a hydraulic conductivity of      6.9 x 10-4m/s and porosity of 30% if the hydraulic gradient is 0.0014?

Solving using Eq. 4-32