Chapter 6 FE EXAM FORMATTED PROBLEMS

6-1.	Three parallel flow flocculation basins are to be used to treat a flow rate of 3 MGD. What is the design volume, in cubic feet, of one of these tanks if the detention time is 30 minutes?

Parallel flow therefore,

The volume of one tank is

6-2. 	Determine the number of rapid sand filters to treat a flow rate of 75.7 x 103 m3/d if the design loading rate is 300 m3/d∙m2. The maximum dimension is 7.5 m and the length to width ratio is 1.2:1.

Assume a length of 7.5m, then

6-3.	Estimate the amount of lime, in tons/d, required to soften 5 MGD of water to the practical solubility limits. The constituent concentrations are as follows:

CO2 = 0.44 meq/L		Alkalinity = 3.96 meq/L

Ca2+ = 4.76 meq/L		Cl- = 1.91 meq/L

Mg2+ = 1.11 meq/L		SO42- = 1.58 meq/L

Lime additions:

Lime = CO2 = 0.44 meq/L

Lime = Alkalinity = 3.96 meq/L

Lime = Mg2+ = 1.11 meq/L

Total Lime = 0.44 + 3.96 + 1.11 = 5.51 meq/L

Equivalent weight of lime:

MW of CaO = 56mg

6-4.	Calculate the theoretical percent removal of a particle having a settling velocity of 0.25 cm/s settling in a horizontal flow clarifier with an overflow rate of 0.05 cm/s.

From Eq. 6-33.