Chapter 9 FE EXAM FORMATTED PROBLEMS

9-1. 	A power plant emits 600g of SO2/s from an effective stack height of 300m. The wind speed at this height is 5.0 m/s. The stability class is C. What is the maximum downwind concentration?

Using Figure 9-27 for C stability and a 300m effective stack height, the maximum concentration occurs at a distance 4km from the stack.

9-2. 	Select an appropriate air to cloth ratio for fly ash and estimate the number of bags required for a gas flow rate of 15m3/s.  Assume each bag is 15 cm in diameter and 5 m in length and that bag cleaning is by pulse jet.

Air to cloth ratio for fly ash using Table 9-19

9-3. 	Estimate the stoichiometeric air to fuel ratio for a 100% ethanol (CH3CH2OH) fuel. One mole of CH3CH2OH = 46g; one mole of O2 = 32g; one mole of N2 = 28g. Assume the following reaction.

6CH3CH2OH + 36O2 + 135.36N2 → 12CO2 + 18H2O + 135.35N2

Ignore the oxidation of Nitrogen

9-4.	Calculate the rate of emission of SO2 in g/s that results in a centerline (y=0) concentration at ground level of 1.412x10-3g/m3 on kilometer from the stack. The time of the measurement was 1 PM on a clear summer afternoon. The wind speed was 1.8m/s measured at a height of 10m. The effective stack height is 94m. No inversion is present.

From Figure 9-24, sy=215m and sz=450m then Solving using Eq. 9-25 with y = 0