Chapter 7 A

1.	T

2.	F

3.	T

4.	F

5.	F

6.	F

7.	T

8.	F

9.	T

10.	D

11.	A

12.	C

13.	A

14.	B

15.	C

16.	There are 4! (Or 1 x 2 x 3 x 4 = 24) possible arrangements of this layout. Since
             the locations of departments are symmetrical, these arrangements can be
             grouped in three sets of eight arrangements each. Each arrangement in a group
             will give the same total cost. Therefore, only three arrangements are to be
             evaluated to determine the layout for which the total cost is a minimum.

For the group belonging to initial layout, the remaining seven arrangements are:

BA	CB	BC	AD	DA	CD	DC

CD	DA	AD	BC	CB	BA	AB

Each one of these arrangements will give the same total cost as that for initial layout.  The total cost for initial layout can be calculated as follows:

Flow Between	Number of	Cost of		Cost of Flow
Departments	Loads		Load		Between Departments

AB		2	           $1	            $ 2

AC		6		 2		 12

AD		8		 1		   8

BC		5		 1		   5

BD		3		 2		   6

CD		1		 1		   1

$34

You can confirm that total cost for each one of the seven arrangements listed above will be $34.

| A | D |
| --- | --- |
| C | B |

The total cost for this arrangement can be calculated as follows:

Flow Between	Number of	Cost of		Cost of	 Flow
Departments	Loads		Load		Between Departments

AB	                2	             $2	                   $ 4

AC		    6		   1		          6

AD		    8		   1		          8

BC		    5		   1		          5

BD		    3		   1		          3

CD		    1		   2		          2

$28

You may like to identify the remaining seven arrangement sin this group and confirm that the total cost for each one of them will be $28.

An arrangement from the third group is given below:

| A | B |
| --- | --- |
| C | D |

The total cost for this arrangement can be calculated as follows:

Flow Between	Number of	Cost of		Cost of Flow
Departments	Loads		Load		Between Departments

AB		   2	             $1	                   $ 2

AC		   6		   1		          6

AD		   8		   2	                    16

BC		   5		   2	                    10

BD		   3		   1		          3

CD		   1		   1		          1

$38

Once again, you may like to identify the remaining arrangements in this group and confirm the total cost for each one will be $38.

Considering all three groups, the total cost is minimum for an arrangement in the second group.

17.	Arrangement:  ACB or BCA; minimum total cost $16.

18.	Cycle time = 12 seconds; number of work stations = 4; efficiency = 95.83
            percent.