# Chapter 19

1.	F

2.	T

3.	T

4.	F

5.	F

6.	F

7.	T

8.	T

9.	T

10.	F

11.	E

12.	A

13.	A

14.	B

15.	B

16.	C

17.	A

18.	D

19.	D

20.	D

21.a.   By the shortest operation time rule, the jobs would be assigned in the following order:  E, B, C, A, D. The flow time is calculated as follows:

| E | B | C | A | D |
| --- | --- | --- | --- | --- |
| 2 | 3 | 4 | 5 | 7 |

Cumulative time in days:

0          2                            5                          9                           14                         21

The mean flow time and mean lateness are calculated as follows:

Job	Flow Time

A	14

B	 5

C	 9
D	21
E	 2
Total	51

Mean flow time = 51/5 or 10.2 days

b.  The first step is to calculate slack time

Job	Due Date	Days of Processing Time   Slack Time (Due Date - Processing time)

A	6 days hence		5				1
B	7 days hence		3				4
C	4 days hence		4				0
D	9 days hence		7				2
E	5 days hence		2				3

By the minimum slack rule the jobs would be assigned in the following order:
 C, A, D, E, B. The flow time is calculated as follows:

| C | A | D | E | B |
| --- | --- | --- | --- | --- |
| 4 | 5 | 7 | 2 | 3 |

Cumulative time in days:

0         4                             9                         16                          18                        21

The mean flow time and mean lateness are calculated as follows:

Job	Flow Time

A	 9

B	21

C	 4
D	16
E	18

Total      68

Mean flow time = 68/5 or 13.6 days

c.  Critical ratio is defined as:  Time Remaining until due date divided by work remaining.

Job	Time Remaining	Work

Until Due date	        Remaining 	     Critical Ratio

A	6 			5			1.20
B	7 			3			2.33
C	4 			4			1.00
D	9 			7			1.29
E	5 			2			2.50

By using the critical ratio, the jobs would be arranged in the following order: C, A, D, B,  E.  The flow time is calculated as follows:

| C | A | D | B | E |
| --- | --- | --- | --- | --- |
| 4 | 5 | 7 | 3 | 2 |

Cumulative time in days:

0                         4                          9                         16                         19                21

The mean flow time is calculated as follows:

Job	Flow Time

A	 9

B	19

C	 4
D	16
E	21

Total      69

Mean flow time = 69/5 or 13.8 days.

d.  The sequence E, B, C, A, D gives minimum flow time and minimum lateness.  The shortest operation time rule always results in minimum mean flow time.

22.  Using Johnson’s rule, we select the jobs in order of shortest operation time and assign them as follows:

Order of		Position In

Selection	Job	Sequence

1		C	6th

2		E	1st

3		B	2nd 
4		F	5th
5		A	4th
6		D	3rd

The jobs would be assigned in the following order:  E, B, D, A, F, C.  The flow times for jobs are shown below:

Machine I

3                       7                  14                      22                  34                 49

| E | B | D | A | F | C |
| --- | --- | --- | --- | --- | --- |

Machine II

| E | B | D | A | F |
| --- | --- | --- | --- | --- |

10                               19                               28     34            39

b.  Slack per remaining operation is defined as:

Time remaining before due date - Remaining machine time

Number of remaining operations

Job		Slack time		Priority

A		49 - (8 + 6) = 17.5	   3rd

2

B		49 - (4 + 9) = 18	   4th

2

C		49 - (15 + 0) = 34	   6th

1

D		49 - (7 + 9) = 16.5	   2nd

2

E		49 - (3 + 7) = 19.5	   5th

2

F		49 - (12 + 5) = 16	   1st

2

The jobs would be assigned in the following order:  F, D, A, B, E, and C. The flow times for jobs are shown below:

Machine I

| F | D | A | B | E | C |
| --- | --- | --- | --- | --- | --- |

12                    19                  27                     31                  34                 49

Machine II

| F | D | A | B | E |
| --- | --- | --- | --- | --- |

17                               28                               34     43            50

Note: There is idle time before both D and A.

c. Critical ratio is defined as: Time remaining until due date

Work Remaining

Job	Critical ratio		Priority

A	49/(8 + 6)   = 3.50	4th

B	49/(4 + 9)   = 3.77	5th

C	49/(15 + 0) = 3.27	3rd

D	49/(7 + 9)   = 3.60	2nd

E	49/(3 + 7)   = 4.90	6th

F	49/(8 + 6)   = 2.88	1st

The jobs would be assigned in the following order: F, D, C, A, B, E. The flow times are shown below:

Machine I

| F | D | C | A | B | E |
| --- | --- | --- | --- | --- | --- |

12                    19                  34                     42                  46                 49

Machine II

| F | D | A | B | E |
| --- | --- | --- | --- | --- |

17                               28                               48     57            64

Note there is idle time before both D and A.

d. Only the Johnson’s rule provides the sequence which would allow all the jobs to be completed before the due date. Johnson’s rule always minimizes the total completion time when two or more jobs much be processed on two machines in a common sequence.