## Slide 1
Electricity
Principles & Applications
Eighth Edition
Chapter 7
Magnetism and
Electromagnetism
(student version)
Richard J. Fowler
McGraw-Hill
© 2013 The McGraw-Hill Companies Inc. All rights reserved.
7 - <number>

## Slide 2
INTRODUCTION
Magnetic Domains (Page 184)
Magnetic Forces (Page 179)
Magnetic Fields (Page 178)
Electromagnetism (Page 181)
Induced Voltage (Page 185)
Reluctance (Page 183)
Magnetic Units (Page 186)
7 - <number>

## Slide 3
Dear Student:
This presentation is arranged in segments. Each segment
is preceded by a Concept Preview slide and is followed by a
Concept Review slide. When you reach a Concept Review
slide, you can return to the beginning of that segment by
clicking on the Repeat Segment button. This will allow you
to view that segment again, if you want to.
7 - <number>

## Slide 4
Concept Preview
Magnetic domains are present in
all magnetic materials. (Page 184)
Magnetic domains are aligned in
all magnetized materials. (Page 184)
Magnetic domains remain aligned in
permanent magnetic materials. (Page 184)
Like magnetic poles repel each other. (Page 179)
7 - <number>

## Slide 5
Facts about Magnetism
Magnetism is an invisible force field.
Most magnets have a north pole and a south pole.
Flux leaves the north pole and enters the south pole.
Like poles repel; unlike poles attract.
Magnetic materials have magnetic domains.
Current-carrying conductors produce magnetic fields.
Magnetic flux follows the path of least reluctance.
7 - <number>

## Slide 6
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
Magnetic Domains in a Magnetic Field
Domains are randomly arranged in this
unmagnetized temporary magnetic material.
When subjected to a magnetic force field,
the domains are aligned with the field.
When the magnetic force field is removed,
the domains return to a random arrangement.
(case 1) (page 184)
7 - <number>

## Slide 7
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
Magnetic Domains in a Magnetic Field
Domains are randomly arranged in this
unmagnetized permanent magnetic material.
When subjected to a magnetic force field,
the domains are aligned with the field.
When the magnetic force field is removed,
the domains remain aligned.
(case 2) (Page 185)
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
S
N
7 - <number>

## Slide 8
Like poles produce a repelling force on these held-in-place magnets. The flux loops are distorted.
Reaction Of Like Poles
(page 179)
S
N
S
N
7 - <number>

## Slide 9
Like poles produce a repelling force
on these held-in-place magnets.
When freed, the magnets move apart
Reaction Of Like Poles (Page 179)
S
N
S
N
and the distortion decreases.
7 - <number>

## Slide 10
Like poles produce a repelling force.
Reaction Of Like Poles
S
N
S
N
The magnets move apart and the distortion decreases.
7 - <number>

## Slide 11
Reaction Of Like Poles
S
N
S
N
Like poles produce a repelling force.
The magnets move apart and the distortion decreases.
7 - <number>

## Slide 12
MAGNETIC FIELD OF A RING MAGNET
(Page 180)
This picture shows a sheet of clear plastic with a sprinkling of iron filings on it.
The next slide shows how the magnetic field of a ring magnet attracts these
filings as the plastic is brought down on the flat surface of a ring magnet.
Notice that the complete surface of the magnet has attraction for the
filings because the whole surface is one pole of the magnet.
Once the plastic sheet is pulled back from the surface, the filings flatten
indicating that the field is getting weaker.
Also notice that the filings are standing up indicating that the field is
radiating from the surface.
7 - <number>

## Slide 13
Watch the action described in the previous slide.
Click play again to see the action repeated.
7 - 13

## Slide 14
Magnetism Quiz
Most magnets have ____ poles.
Flux leaves the ____ pole of a magnet.
Like magnetic poles ____ each other.
Magnetic materials have magnetic ____.
A magnetic force field contains ____.
two
north
repel
domains
flux
In non-magnetized magnetic materials
the_____ are randomly arranged.
domains
7 - <number>

## Slide 15
Concept Review
Magnetic domains are present in
all magnetic materials.
Magnetic domains are aligned in
all magnetized materials.
Magnetic domains remain aligned in
permanent magnetic materials.
Like magnetic poles repel each other.
Repeat Segment
7 - <number>

## Slide 16
Concept Preview
A current-carrying conductor produces
magnetic flux rings around itself. (Page 181)
Parallel conductors repel each other when
their currents are in opposite directions.
(P 182)
Parallel conductors attract each other if
their currents are in same directions. (Page 182)
The direction of the current in a conductor
determines the direction of the flux. (Page 181)
7 - <number>

## Slide 17




Electromagnetism (page 181)
Direction
of current
Conductor
Current in a conductor
produces flux around the conductor.
A larger current
produces more flux.
Use the left-hand rule to determine
the direction of the flux.
7 - <number>

## Slide 18
Flux Around Parallel Conductors
(Page 182)
The conductors repel each other when
the currents are in opposite directions.






7 - <number>

## Slide 19






The conductors repel each other when
the currents are in opposite directions.
Flux Around Parallel Conductors
7 - <number>

## Slide 20






The conductors repel each other when
the currents are in opposite directions.
Flux Around Parallel Conductors
7 - <number>

## Slide 21






The conductors repel each other when
the currents are in opposite directions.
Flux Around Parallel Conductors
7 - <number>

## Slide 22
The conductors attract each other when
the currents are in the same direction.
Flux Around Parallel Conductors





7 - <number>

## Slide 23




The conductors attract each other when
the currents are in the same direction.
Flux Around Parallel Conductors
7 - <number>

## Slide 24




Flux Around Parallel Conductors
The conductors attract each other when
the currents are in the same direction.
7 - <number>

## Slide 25
Electromagnetism Quiz
Current-carrying conductors produce
magnetic ____.
The flux around a conductor ____
as the current increases.
The ____ rule is used to determine
the flux direction around a conductor.
Parallel conductors ____ each other when
the currents are in the same direction.
flux
left-hand
increases
attract
7 - <number>

## Slide 26
Concept Review
A current-carrying conductor produces
magnetic flux rings around itself.
Parallel conductors repel each other when
their currents are in opposite directions.
Parallel conductors attract each other if
their currents are in same directions.
The direction of the current in a conductor
determines the direction of the flux.
Repeat Segment
7 - <number>

## Slide 27
Concept Preview
Magnetic flux will seek a short path
that has low reluctance. (Page 188)
Voltage is induced in a conductor that
cuts magnetic flux. (Page 190)
Lines of flux will follow a distorted path
if it is a short, low-reluctance path. (Page 188)
Both the directions of the flux and the
conductor movement determine the
polarity of the induced voltage. (Page 191)
7 - <number>

## Slide 28
Flux
Low-Reluctance Flux Path
(Page 189)
Flux bends to follow a low-reluctance path.
Iron
7 - <number>

## Slide 29
N
S
Adding a Low-Reluctance Path in a Magnetic Field.
(Page 188)
Opposite magnetic poles produce a
flux in the air between the poles.
When a low-reluctance path is provided, the flux increases
and is concentrated in the low-reluctance path.
7 - <number>

## Slide 30

X
Induced Voltage
(Page 189)
Voltage is induced when conductors cut lines of flux.
Green arrow shows direction of conductor movement.
Dot and X show direction of current caused by voltage.
No voltage is induced when conductors move parallel
to the to the lines of flux.
7 - <number>

## Slide 31
Repeat Segment
Concept Review
Magnetic flux seeks a short path
with low reluctance.
Voltage is induced in a conductor that
cuts magnetic flux.
Lines of flux will follow a distorted path
if it is a short, low-reluctance path.
Both the directions of the flux and the
conductor movement determine the
polarity of the induced voltage.
7 - <number>

## Slide 32
Different size magnetic cores can
accommodate the same flux density. (Page 194)
Different size magnetic cores can have
the same magnetic field strength. (Page 193)
The permeability of a material is
independent of the size of the material. (Page 194)
Relative permeability has no units. (Page 194)
Concept Preview
7 - <number>

## Slide 33
Magnetic Quantities and Units
magnetomotive force (mmf)
magnetic field strength (H)
flux ()
flux density (B)
permeability ()
relative permeability
QUANTITIES
UNITS
ampere-turn (t)
ampere-turn/meter (At/m)
weber (Wb)
tesla (T)
Wb/(Atm)
unitless
Page 192
7 - <number>

## Slide 34
3 A
3 A
Magnetic Field Strength (Page 193)
mmf = 3 A x 8 t = 24 At
mmf = 3 A x 4 t = 12 At
Core length = 0.4 m
Core length = 0.2 m
H =
24 At
0.4 m
=
60 At / m
H =
12 At
0.2 m
=
60 At / m
The magnetic field strength is the same for the two circuits.
8 t
4 t
7 - <number>

## Slide 35
Flux Density (Page 193)
Material B carries twice as much flux as material A.
However, the flux density (B) is the same in both materials because the cross-sectional area of B is two times larger than that of A.
A
B
7 - <number>

## Slide 36
Quantities and Units Quiz
The opposition to flux is called ____.
The unit of flux is the ____.
Flux density is specified in ____.
Wb/(Atm) is the unit for ____.
The symbol for magnetic field strength is ____.
The symbol for flux density is ____.
The value of H is ____ when I = 4A ,
N = 12t , and l = 0.2m.
reluctance
weber
tesla
permeability
H
B
240 At/m
7 - <number>

## Slide 37
Repeat Segment
Different size magnetic cores can
accommodate the same flux density.
Different size magnetic cores can have
the same magnetic field strength.
The permeability of a material is
independent of the size of the material.
Relative permeability has no units.
Concept Review
7 - <number>

## Slide 38
REVIEW
Magnetic Domains
Magnetic Forces
Magnetic Fields
Electromagnetism
Induced Voltage
Reluctance
Magnetic Units
7 - <number>