## Slide 1
Electricity
Principles & Applications
Eighth Edition
Chapter 10
Capacitance
(student version)
Richard J. Fowler
McGraw-Hill
© 2013 The McGraw-Hill Companies Inc. All rights reserved.
10 - <number>

## Slide 2
INTRODUCTION
Capacitor Terminology
Use of Capacitors
Capacitors in Ac and Dc Circuits
Series and Parallel Capacitors
Time Constants
Capacitive Reactance
10 - <number>

## Slide 3
Dear Student:
This presentation is arranged in segments. Each segment
is preceded by a Concept Preview slide and is followed by a
Concept Review slide. When you reach a Concept Review
slide, you can return to the beginning of that segment by
clicking on the Repeat Segment button. This will allow you
to view that segment again, if you want to.
10 - <number>

## Slide 4
Concept Preview
A capacitor has two plates and
a dielectric. (Page 251)
Dielectric materials are insulators. (Page 251)
A capacitor charges until its voltage
equals the source voltage. (Page 250)
Battery current decays to zero as the
the capacitor charges. (Page 262)
Capacitors can cause a large surge
current. (Page 263)
10 - <number>

## Slide 5
Facts About Capacitance
Capacitance stores electric energy.
The dielectric material blocks current flow between
the plates of a capacitor.
The base unit of capacitance is the farad.
Most electrolytic capacitors are polarized.
A capacitor’s opposition to current is called reactance.
The ohm is the base unit of reactance.
Capacitance causes current to lead voltage by 90.
W = 0.5CV2
XC = 1/(6.28fC)
10 - <number>

## Slide 6
Construction of a Capacitor
Lead
Lead
Plate
Plate
Dielectric
The plates and leads are conductors.
The dielectric is an insulator.
(Page 251)
10 - <number>

## Slide 7
Charging A Capacitor (Page 250)
Current flows
and the capacitor charges
-
+
until its voltage equals the source voltage.
15 V
15 V
At this time the current stops.
IC
VC
15 V
0
Time
Notice that I is maximum when V is minimum and visa versa.
Imax is very large when C is large and a high-current source is used.
10 - <number>

## Slide 8
Capacitor-Current Quiz
The ____ of a capacitor is an insulator.
The capacitor current ____ as the capacitor
voltage increases.
When charged, the capacitor voltage equals
the ____ voltage.
Charging current is controlled by the value
of ____ and the current capacity of the source.
The base unit of capacitance is the ____.
dielectric
farad
decreases
source
capacitance
10 - <number>

## Slide 9
Concept Review
Repeat Segment
A capacitor has two plates and a dielectric.
Dielectric materials are insulators.
A capacitor charges until its voltage
equals the source voltage.
Battery current decays to zero as the
the capacitor charges.
Capacitors can cause a large surge current.
10 - <number>

## Slide 10
Concept Preview
A charged capacitor stores energy in
its distorted dielectric material. (Page 252)
Increasing the plate area of a capacitor
will increase its capacitance. (Page 255)
Increasing the plate spacing of a capacitor
will decrease its capacitance. (Page 255)
An electric field between the plates of a
capacitor stresses the dielectric material.
(Page 252)
10 - <number>

## Slide 11
Electric Field Of A Charged Capacitor
(Page 251)
Dielectric
material
The electric field ( )
stresses the
dielectric
material.
Lead
Plate
Lead
Plate
+ + + + + + + + + + +
- - - - - - - - - - -
First, construct
a capacitor and
note its parts.
Next, charge the
capacitor and
observe the electric
field.
10 - <number>

## Slide 12
Stressed Dielectric Material (Page 252)
Lead
Plate
- - - - - - - - - - - - -
+ + + + + + + + + + + + +
Plate
Lead
+
-
+
-
+
-
+
-
The distorted orbital paths increase the energy level of the electrons.
The capacitor stores energy in its distorted dielectric material.
10 - <number>

## Slide 13
Plate area
More capacitance
Spacing of plates
Less capacitance
Dielectric material
More capacitance
Air
Mica
Physical Factors Affecting Capacitance
(Page 255)
10 - <number>

## Slide 14
Capacitor-Value Quiz
A charged capacitor produces
a(n) ____ ____ between its plates.
A charged capacitor stores energy in its ____.
Charging a capacitor increases the energy
level of the ____ in the dielectric.
Increasing the plate area ____ the capacitance.
Increasing the distance between the
plates _____ the capacitance.
electric field
dielectric
electrons
increases
decreases
10 - <number>

## Slide 15
Concept Review
Repeat Segment
An electric field between the plates of a
capacitor stresses the dielectric material.
A charged capacitor stores energy in
its distorted dielectric material.
Increasing the plate area of a capacitor
will increase its capacitance.
Increasing the plate spacing of a capacitor
will decrease its capacitance.
10 - <number>

## Slide 16
Concept Preview
A filter capacitor can smooth out
pulsating direct current. (Page 260)
As a capacitor charges, it takes energy
from the source. (Page 266)
As a capacitor discharges, it returns
its stored energy to the source. (Page 267)
After five time constants, a capacitor
is essentially charged or discharged.
(Page 264)
10 - <number>

## Slide 17
Pulsating dc before filtering
After filtering
V
t
V
t
Action Of A Filter Capacitor
(Page 260)
10 - <number>

## Slide 18
Electrolytic Capacitor
Venting plug on this end
This capacitor is about to be reverse-
connected to a 15-V dc supply. (Page 256)
Watch the venting plug in this series of slides.
10 - <number>

## Slide 19
Reverse voltage has been applied for about 25 seconds.
Notice the venting plug is being pushed out.
The next slide shows the last 5 seconds
of the life of this capacitor.
10 - <number>

## Slide 20
( Watch the venting plug )
(Please wait for the image to load and display.)
Click play to rerun the video.
10 - <number>

## Slide 21
Telephoto view after the smoke has cleared.
( For protection, the capacitor was under a piece of glass.)
10 - <number>

## Slide 22
100
0
% of source voltage
Time constants
0
1
2
3
4
5
After 1 T, the capacitor is 63.2 % charged.
After 2 T, the capacitor is 86.5 % charged.
After 3 T, the capacitor is 95.0 % charged.
After 4 T, the capacitor is 98.2 % charged.
After 5 T, the capacitor is 99.3 % charged.
The capacitor is essentially charged after 5 T.
RC Time Constant -- Charge
(Page 263)
10 - <number>

## Slide 23
After 1 T, the capacitor is 63.2 % discharged.
After 2 T, the capacitor is 86.5 % discharged.
After 3 T, the capacitor is 95.0 % discharged.
After 4 T, the capacitor is 98.2 % discharged.
After 5 T, the capacitor is 99.3 % discharged.
The capacitor is essentially discharged after 5 T.
Time constants
0
1
2
3
4
5
100
0
% of capacitor voltage
36.8%
13.5%
5.0%
1.8%
0.7%
RC Time Constant – Discharge (Page 264)
10 - <number>

## Slide 24
-
+
-
+
I
During the first quarter of the cycle, the current decreases
as the voltage increases.
needed to charge the capacitor.
The source is providing the energy
When the voltage reaches its
peak value, there is no current.
V
Energy Transfer In A Capacitor Circuit
(Page 266)
10 - <number>
Notes: <number>

## Slide 25
-
+
-
+
I
V
Energy Transfer In A Capacitor Circuit
During the second quarter-cycle,
the capacitor returns its energy
to the source.
Notice that the current has changed direction.
Also notice that the current is now increasing while the
voltage is decreasing.
Second quarter-cycle
10 - <number>

## Slide 26
-
+
-
+
I
V
Energy Transfer In A Capacitor Circuit
During the third quarter-cycle,
the source provides the energy
to charge the capacitor.
Notice that the current has not changed
direction. It is now decreasing while the voltage is increasing.
Third quarter-cycle
10 - <number>

## Slide 27
-
+
-
+
I
V
Energy Transfer In A Capacitor Circuit
During the fourth quarter-cycle,
the capacitor returns its energy
to the source.
Notice that the current has changed direction.
Also notice that the current is now increasing while the
voltage is decreasing.
Fourth quarter-cycle
10 - <number>

## Slide 28
Capacitor-Action Quiz
A filter capacitor changes pulsating dc
into ____ dc.
After one time constant a capacitor
is ____ % charged.
A capacitor is essentially charged
after ____ time constants.
In an ac circuit, a capacitor returns energy
to the source ____ each cycle.
With an ac source, the capacitor voltage ____
while the capacitor current increases.
fluctuating
63.2
five
twice
decreases
10 - <number>

## Slide 29
Concept Review
Repeat Segment
A filter capacitor can smooth out
pulsating direct current.
After five time constants, a capacitor
is essentially charged or discharged.
As a capacitor charges, it takes energy
from the source.
As a capacitor discharges, it returns
its stored energy to the source.
10 - <number>

## Slide 30
Concept Preview (Page 263)
The smallest series C drops the most V.
The largest parallel C draws the most I.
XC is inversely proportional to C and f.
In a relaxation oscillator, the capacitor
charges until the NE-2 fires.
10 - <number>

## Slide 31
Voltage Distribution In Series Capacitors
(Pages 265 and 273)
60 V
60 V
2 F
40 V
4 F
20 V
2 F
40 V
4 F
20 V
In either a dc
or an ac
series circuit,
the smallest capacitor
develops the most voltage.
The voltage distributes in inverse
proportion to the capacitance.
10 - <number>

## Slide 32
Current Distribution In Parallel Capacitors
(Page 274)
or an ac
parallel circuit,
the largest capacitor
draws the most current.
The current distributes in direct
proportion to the capacitance.
60 V
2 F
2 A
4 F
4 A
2 F
0.2 A
4 F
0.4 A
60 V
In either a dc
Peak charging I
10 - <number>

## Slide 33
k

mA
mV
V
A
+ V A 
COM -
d c
a c
2 F
40 V
100 Hz
40 V
F
100 Hz
Measure the current when C is 2F.
Next, calculate XC.
XC = VC / IC = 40 V / 50.24 mA = 796 
Measure the current when C is 1F.
Then, calculate XC.
XC = 40 V / 25.12 mA = 1592 
Notice that XC is inversely proportional to C.
Capacitive Reactance And Capacitance
(Page 267)
10 - <number>

## Slide 34
k

mA
mV
V
A
+ V A 
COM -
d c
a c
2 F
40 V
100 Hz
40 V
F
50 Hz
Measure the current when f is 100 Hz.
Next, calculate XC.
XC = VC / IC = 40 V / 50.24 mA = 796 
Measure the current when f is 50 Hz.
Then, calculate XC.
XC = 40 V / 25.12 mA = 1592 
Notice that XC is inversely proportional to f.
Capacitive Reactance And Frequency
(Page 268)
10 - <number>

## Slide 35
Relaxation Oscillator Circuit (Page 276)
When power is applied, the capacitor charges to the firing voltage
of the NE-2
and produces part of the sawtooth waveform.
When the NE-2 fires, the capacitor discharges through the NE-2,
the source sends current through the NE-2 and the resistor,
and the rest of the sawtooth waveform is produced.
Then the cycle starts over.
NE-2
NE-2
10 - <number>
Notes: <number>

## Slide 36
Capacitor-Circuit Quiz
In a series capacitor circuit, the smallest
capacitor develops the ____ voltage.
In a parallel capacitor circuit, the smallest
capacitor draws the ____ current.
Increasing capacitance ____ reactance.
Increasing frequency ____ reactance.
Circuit current in a capacitor circuit will ____
when the frequency is decreased.
The reactance of a 2 F capacitor at 200 Hz
is ____ ohms.
most
least
decreases
decreases
decrease
398
10 - <number>

## Slide 37
Concept Review
Repeat Segment
The smallest series C drops the most V.
The largest parallel C draws the most I.
XC is inversely proportional to C and f.
In a relaxation oscillator, the capacitor
charges until the NE-2 fires.
10 - <number>

## Slide 38
REVIEW
Capacitor Terminology
Use of Capacitors
Capacitors in Ac and Dc Circuits
Series and Parallel Capacitors
Time Constants
Capacitive Reactance
10 - <number>