## Slide 1
Electricity
Principles & Applications
Eighth Edition
Chapter 11
Inductance
(student version)
Richard J. Fowler
McGraw-Hill
© 2013 The McGraw-Hill Companies Inc. All rights reserved.
11 - <number>

## Slide 2
INTRODUCTION
Polarity of Induced Voltage
Inductive Reactance
Series and Parallel Inductors
Skin Effect
Mutual Inductance
11 - <number>

## Slide 3
Dear Student:
This presentation is arranged in segments. Each segment
is preceded by a Concept Preview slide and is followed by a
Concept Review slide. When you reach a Concept Review
slide, you can return to the beginning of that segment by
clicking on the Repeat Segment button. This will allow you
to view that segment again, if you want to.
11 - <number>

## Slide 4
Concept Preview
Cemf opposes the source V as I increases. (Page 283)
Cemf aids the source V as I decreases. (Page 284)
Steady state dc is unopposed by inductance. (Page 293)
Inductance controls the rate at which a
direct current can rise or fall. (Page 293)
The current in a dc inductor circuit is
determined by the R of the inductor. (Page 293)
11 - <number>

## Slide 5
Facts About Inductors
Magnetic fields store energy.
An inductor provides self-inductance.
Self-induced voltage is called cemf or bemf.
When an inductor induces a voltage in another
inductor it is called mutual inductance.
Lenz’s law shows that a cemf opposes the force that created it.
The base unit of inductance (L) is the henry (H).
Inductance (L) has inductive reactance (XL).
XL = 6.28fL
Inductance causes voltage to lead current by 90 degrees.
11 - <number>

## Slide 6




Polarity Of Induced Voltage (Page 285)
Direction
of current
Conductor
When current increases and flux expands,
the polarity of the
self-induced voltage (cemf) is negative where the current enters.
Notice that the cemf opposes the increasing source voltage that
is causing the current to increase and the flux to expand.
+
polarity of cemf
11 - <number>

## Slide 7


Polarity Of Induced Voltage (Page 285)
Conductor
When current decreases and flux collapses,


11 - <number>

## Slide 8

Polarity Of Induced Voltage
Direction
of current
Conductor
When current decreases and flux collapses,
the polarity of the self-induced voltage (cemf) is positive where the current enters.
Notice that the cemf aids the decreasing source voltage that
is causing the current to decrease and the flux to collapse.
+
polarity of cemf

11 - <number>

## Slide 9
Inductive Current in a DC Circuit (Page 293)
I
t
0
When the switch is closed,
rate at witch the current can rise.
the inductor limits the
While the switch remains closed, the current is steady at a
value determined by the applied V and the R of the inductor.
When the switch is opened,
the rate at which the current can fall.
the inductor limits
11 - <number>

## Slide 10
Concept Review
Repeat Segment
Cemf opposes the source V as I increases.
Cemf aids the source V as I decreases.
Steady state dc is unopposed by inductance.
Inductance controls the rate at which a
direct current can rise or fall.
The current in a dc inductor circuit
is determined by the R of the inductor.
11 - <number>

## Slide 11
Concept Preview
Inductance takes energy from the source
while its flux builds up. (Page 285)
Inductance returns energy to the source
when its flux decays. (Page 285)
I lags V by 90 in an inductive circuit. (Page 296)
In an inductive circuit, I increases
while V is decreasing. (Page 296)
11 - <number>

## Slide 12
-
+
-
+
V
During the first quarter of the cycle, the current increases
as the voltage decreases.
needed to create the inductor’s flux and cemf.
The source is providing the energy
When the current reaches its peak value, there is no voltage.
I
Energy Transfer In An Inductor Circuit
(Page 285)
11 - <number>

## Slide 13
-
+
-
+
Energy Transfer In An Inductor Circuit
V
I
During the second quarter-cycle,
to the source.
Notice that the voltage has changed polarity.
Also notice that the current is now decreasing while the
voltage is increasing.
the inductor returns its energy
Second quarter-cycle
11 - <number>

## Slide 14
-
+
-
+
Energy Transfer In An Inductor Circuit
V
I
During the third quarter-cycle,
the source provides the energy
needed to create the inductor’s flux and cemf.
Notice that the voltage has not changed polarity.
It is now decreasing while the reversed current is increasing.
Third quarter-cycle
11 - <number>

## Slide 15
-
+
-
+
Energy Transfer In An Inductor Circuit
V
I
During the fourth quarter-cycle,
to the source.
Notice that the voltage has changed polarity.
Also notice that the current is now decreasing while the
voltage is increasing.
the inductor returns its energy
Fourth quarter-cycle
11 - <number>

## Slide 16
Variable Inductance (Page 288)
The lamp and the inductor are in series with an ac supply. The
inductance does not allow enough current to light the lamp.
The next slide shows that removing the I laminate decreases
the inductance so that the lamp operates at almost full brilliance.
<number>
11 - <number>

## Slide 17
(Please wait for the image to load and display.)
Click play to rerun the display.
11 - <number>

## Slide 18
Inductor-Action Quiz
The self-induced voltage of an inductor is
called ____.
The cemf ____ a decreasing source voltage.
During the second quarter-cycle, the ____ provides
the energy in an inductor circuit.
Current and voltage are ____ degrees out-of-phase
in an inductor circuit.
Current ____ voltage in an inductive circuit.
cemf
aids
inductor
90
lags
11 - <number>

## Slide 19
Concept Review
Repeat Segment
Inductance takes energy from the source
while its flux builds up.
Inductance returns energy to the source
when its flux decays.
I lags V by 90 in an inductive circuit.
In an inductive circuit, I increases
while V is decreasing.
11 - <number>

## Slide 20
Concept Preview
XL is directly proportional to L. (Page 295)
XL is directly proportional to f. (Page 295)
Ohm’s law for inductive circuits
is I = V / XL . (Page 296)
In an RL circuit, current has essentially
reached its final value in 5 T. (Page 302)
11 - <number>

## Slide 21
Inductive Reactance And Inductance (Page 295)
k

mA
mV
V
A
+ V A 
COM -
d c
a c
Measure the current when L is 1 H.
Next, calculate XL.
XL = VL / IL = 30 V / 47.77 mA = 628 
Measure the current when L is 2 H.
Then, calculate XL.
XL = 30 V / 23.89 mA = 1256 
Notice that XL is directly proportional to L.
30 V
100 Hz
1H
30 V
100 Hz
2H
11 - <number>

## Slide 22
Inductive Reactance And Frequency (Page 295)
k

mA
mV
V
A
+ V A 
COM -
d c
a c
Measure the current when f is 100 Hz.
Next, calculate XL.
XL = VL / IL = 30 V / 47.77 mA = 628 
Measure the current when f is 200 Hz.
Then, calculate XL.
XL = 30 V / 23.89 mA = 1256 
Notice that XL is directly proportional to f.
30 V
100 Hz
1H
30 V
200 Hz
1H
11 - <number>

## Slide 23
RL Time Constant -- Rising I (Page 302)
100
0
% of final current
Time constants
0
1
2
3
4
5
After 1 T, the inductor’s current is 63.2 % of final value.
After 2 T, the inductor’s current is 86.5 % of final value.
After 3 T, the inductor’s current is 95.0 % of final value.
After 4 T, the inductor’s current is 98.2 % of final value.
After 5 T, the inductor’s current is 99.3 % of final value.
The current has essentially reached its final value after 5 T.
11 - <number>

## Slide 24
After 1 T, the current is reduced by 63.2 % .
After 2 T, the current is reduced by 86.5 % .
After 3 T, the current is reduced by 95.0 % .
After 4 T, the current is reduced by 98.2 % .
After 5 T, the current is reduced by 99.3 % .
The current is essentially zero after 5 T.
Time constants
0
1
2
3
4
5
100
0
% of starting current
36.8%
13.5%
5.0%
1.8%
0.7%
RL Time Constant -- Falling I (Page 302)
11 - <number>

## Slide 25
Reactance and Time-Constant Quiz
When the frequency is doubled, the inductive
reactance ____.
When the inductance is decreased, the inductive
reactance ____.
The I in an inductor circuit will be unchanged
when the f is halved and the L is ____.
The current in an RL circuit will be 99.3 %
of its final value after ____ time constant(s).
The current in an RL circuit decays to 36.8 %
of its maximum value in _____ time constant(s).
doubles
decreases
doubled
five
one
11 - <number>

## Slide 26
Concept Review
Repeat Segment
XL is directly proportional to L.
XL is directly proportional to f.
Ohm’s law for inductive circuits
is IL = VL / XL .
In an RL circuit, current has essentially
reached its final value in 5 T.
11 - <number>

## Slide 27
Concept Preview
The largest series inductance drops
the most voltage. (Page 300)
The smallest parallel inductance
draws the most current. (Page 301)
The skin effect increases the R of an
inductor as the f increases. (Page 298)
Mutual inductance can be controlled
by shielding, orientation, and spacing.
(Page 303)
11 - <number>

## Slide 28
0.1 H
0.3 H
15 V
45 V
In a series inductor circuit,
the largest inductor
develops the most voltage.
The voltage distributes in
direct proportion to the inductance.
60 V
50 Hz
Voltage Distribution In Series Inductors (Page 290)
11 - <number>

## Slide 29
Current Distribution In Parallel Inductors (Page 291)
In a parallel inductor circuit,
the smallest inductor
draws the most current.
The current distributes in
inverse proportion to the inductance.
20 V
200 Hz
0.2 H
0.6 H
79.5 mA
26.5 mA
11 - <number>

## Slide 30
Skin Effect (Page 298)
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
Solid conductor
Solid conductor
At low frequencies, the electrons
At high frequencies, the electrons
are randomly located.
concentrate at the surface.
11 - <number>

## Slide 31
Controlling Mutual Inductance (Page 303)
Axis aligned
Cores touching
Max. Lm
Cores separated
Reduced Lm
Axis perpendicular
Even less Lm
Separated
Shielded
Min. Lm
Perpendicular
11 - <number>

## Slide 32
Mutual Inductance (Page 303)
The ferrite-core inductor is positioned so that maximum
flux from the iron-core inductor is coupled to it.
In the next slide, observe what happens to the induced
voltage as the ferrite-core inductor is pulled away.
11 - <number>

## Slide 33
(Please wait for the image to load and display.)
Click play to rerun the display.
11 - <number>

## Slide 34
Miscellaneous-Concepts Quiz
The ____ inductor develops the most voltage
in a series ac circuit.
The ____ inductor draws the most current
in a parallel ac circuit.
A conductor’s resistance ____ as the frequency
of the current increases.
At ____ frequencies, electrons tend to
leave the center of the conductor.
Two inductors positioned end-to-end have ____
mutual inductance than when they are
positioned at a right angle.
largest
smallest
increases
high
more
11 - <number>

## Slide 35
Concept Review
Repeat Segment
The largest series inductance drops
the most voltage.
The smallest parallel inductance
draws the most current.
The skin effect increases the R of an
inductor as the f increases.
Mutual inductance can be controlled
by shielding, orientation, and spacing.
11 - <number>

## Slide 36
REVIEW
Polarity of Induced Voltage
Inductive Reactance
Series and Parallel Inductors
Skin Effect
Mutual Inductance
11 - <number>