## Slide 1
Electricity
Principles & Applications
Eighth Edition
Chapter 14
Electric Motors
(student version)
Richard J. Fowler
McGraw-Hill
© 2013 The McGraw-Hill Companies Inc. All rights reserved.
14 - <number>

## Slide 2
INTRODUCTION
Motor Ratings
Parts of a Motor
Rotating Magnetic Fields
Split-Phase Motors
Dc Motors
14 - <number>

## Slide 3
Dear Student:
This presentation is arranged in segments. Each segment
is preceded by a Concept Preview slide and is followed by a
Concept Review slide. When you reach a Concept Review
slide, you can return to the beginning of that segment by
clicking on the Repeat Segment button. This will allow you
to view that segment again, if you want to.
14 - <number>

## Slide 4
Concept Preview
R in the supply lines can reduce motor
voltage to an unacceptable level. (Page 374)
A split-phase motor has two windings,
a rotor, and a start-switch mechanism. (Page 384)
While running, flux is created by both
transformer and generator action. (Page 388)
While starting, both windings add to the
flux except when one current is crossing
its zero reference line. (Page 386)
14 - <number>

## Slide 5
Facts About Motors
Some motors can operate on either ac or dc power.
Motors come in either sfhp, fhp, or ihp sizes.
Common motor ratings are voltage, current, power,
temperature, service factor and duty cycle.
A motor’s voltage rating usually has a tolerance of 10 %.
The NEMA establishes standards for motor ratings.
Motors are commonly designed for an ambient
temperature of 40C.
Locked-rotor current is many times greater than
full-load current.
Three-phase motors can be reversed by switching
any two of the three power leads.
14 - <number>

## Slide 6
Voltage Drop In Supply Lines (Page 374)
Source
Motor
Line
resistance
The line resistance
of the cable or cord must be considered when connecting a motor to a source.
Vrated = 230 V
Vmin = 207 V
Vrated = 240 V
Vmin = 220 V
Irated = 18 A
Example:
For the given source voltages,
motor current,
and motor voltages,
determine the maximum resistance
of the cable connected to the motor.
Rmax =
(220 V - 207 V)
/ 18 A =
0.722 
14 - <number>

## Slide 7
Major Parts Of A 1740-RPM Ac Motor
This split-phase motor has a stator,
a 4-pole run winding,
a 4-pole start winding,
and a squirrel-cage rotor on a shaft.
The start switch and centrifugal actuator are not shown.
14 - <number>

## Slide 8
Start Switch Activator (Page 390)
Weight mechanism that pulls bobbin toward rotor.
Bobbin
Switch lever
Spring to hold
switch open
Rotor
Spring holding
weights together
and bobbin against
switch lever.
14 - <number>

## Slide 9
Start Switch Actuator in Action
(Please wait for image to load and display)
Click play if the video does not start automatically.
14 - <number>

## Slide 10
A Rotating Magnetic Field (Page 386)
t1
Time 1
N
S
N
At time 1, current flows only in the run winding.
Therefore, the flux lines up with the centers of the run poles.
The center of the north pole is at the top of the stator.
The start winding does not contribute to the magnetic field.
14 - <number>

## Slide 11
A Rotating Magnetic Field
t2
At time 2, both the run-winding and the start-winding currents
are creating flux.
S
N
The center of the N pole has rotated 45 degrees clockwise.
Time 2
N
S
Therefore, the flux is centered midway between
the centers of the run and start poles.
Notice that the sine wave has also advanced 45 degrees.
N
t1
14 - <number>

## Slide 12
A Rotating Magnetic Field
t3
At time 3, the run- winding current is zero.
Only the start winding is producing flux at this time.
S
N
The center of the N pole has rotated another 45 degrees clockwise.
Time 3
N
t1
t2
14 - <number>

## Slide 13
A Rotating Magnetic Field
t4
At time 4, both windings again have current and are creating flux.
S
N
The center of the N pole has rotated another 45 degrees clockwise.
Time 4
S
N
However, both the run current & the run-pole polarity have reversed.
The flux is again midway between the centers of the poles.
N
t1
t2
t3
14 - <number>

## Slide 14
Creating Rotational Torque (Page 383)
The stator coils
try to create a
flux in the rotor
in this direction.
At the same time,
generator action of
the rotating stator
flux induces rotor
currents that try to
create a flux in
this direction.
Direction of flux rotation
The interaction
of these two
fluxes create a
single flux in
this direction
in the rotor.
Looking at both the
stator and the rotor
shows the distorted
path the flux is forced
to take.
N
S
Torque results
as the flux seeks to
shorten its path.
14 - <number>

## Slide 15
Ratings and Fields Quiz
The voltage rating of motor has a tolerance
of 
10
A maximum line resistance of ____  will
allow a motor rated at 210 Vmin , and 8 Amax ,
to operate from a 220-Vmin source.
1.25
A split-phase stator has ____ windings.
two
The flux created by the run and start windings
produces a ____ magnetic field.
rotating
In a two-pole motor, the flux rotates ____
mechanical  for every 45 electrical  .
45
A 1740-rpm motor has ____ poles in the
run winding.
four
14 - <number>

## Slide 16
Concept Review
Repeat Segment
R in the supply lines can reduce motor
voltage to an unacceptable level.
A split-phase motor has two windings,
a rotor, and a start-switch mechanism.
While running, flux is created by both
transformer action and generator action.
While starting, both windings add to the
flux except when one current is crossing
its zero reference line.
14 - <number>

## Slide 17
Concept Preview
In a split-phase motor, different Q values
cause Irun and Istart to be out-of-phase. (Page 387)
In a split-phase motor, Irun lags Istart by about
20 to 30 degrees. (Page 388)
In a capacitor-start motor, the capacitor in
the start-winding causes Istart to lead Vsource . (Page 391)
In a capacitor-start motor, Irun lags Istart
by about 90 degrees. (Page 391)
14 - <number>

## Slide 18
Split-Phase-Motor Currents (Page 386)
A split-phase motor has a run winding
and a start winding.
Because a winding has both inductance
and resistance,
it also has Q.
The Q of the run winding causes more phase shift
than the Q of the start winding does.
This causes the start current to be out-of-phase with the run current.
Vsource
Irun
Istart
Isource
Lrun
Lstart
Rrun
Rstart
14 - <number>

## Slide 19
The run winding
Vsource
Irun
Istart
Lrun
Rrun
Lstart
Rstart
Isource
Adding a capacitor to the start circuit
causes Istart to lead Vsource .
causes nearly 90 degrees of phase shift.
This causes Istart and Irun to be about 90 out-of-phase.
This results in more starting torque and less
source current to start the motor.
Capacitor-Start-Motor Currents
(Page 391)
14 - <number>

## Slide 20
Motor-Currents Quiz
The Q of the run winding is ____ than the Q of
the start winding in a split-phase motor.
greater
Irun ____ Istart in a split-phase motor.
lags
A capacitor-start motor requires ____ Isource
to start than does a split-phase motor.
less
A capacitor-start motor provides ____ phase shift
between windings than does a split-phase motor.
more
A capacitor-start motor has ____ starting torque
than does a split-phase motor.
more
14 - <number>

## Slide 21
Concept Review
Repeat Segment
In a split-phase motor, different Q values
cause Irun and Istart to be out-of-phase.
In a split-phase motor, Irun lags Istart
by about 20 to 30 degrees.
In a capacitor-start motor, the capacitor in
the start-winding causes Istart to lead Vsource .
In a capacitor-start motor, Irun lags Istart
by about 90 degrees.
14 - <number>

## Slide 22
Concept Preview
The relay coil is in the run winding when
the start winding is relay controlled. (Page 390)
In a permanent-split capacitor motor,
the capacitor can be in either winding. (Page 393)
The two-value-capacitor motor has the
desirable characteristics of the capacitor-start
and the permanent-capacitor motors. (Page 394)
The compound dc motor has the desirable
characteristics of the series dc and the
parallel dc motors. (Page 399)
14 - <number>

## Slide 23
Relay-Controlled Start Winding (Page 390)
”
”
”
”
Rotor
Start
winding
Run
winding
Relay
Note that the relay coil is in
series with the run winding.
14 - <number>

## Slide 24
Relay-Controlled Start Winding
”
”
”
”
Rotor
Start
winding
Run
winding
Relay
Note that the relay coil is in
series with the run winding.
When power is applied, the
large current in the relay
coil closes the relay and
applies power to the start
winding. Watch the relay.
14 - <number>

## Slide 25
Relay-Controlled Start Winding
”
”
”
”
Rotor
120 V
60 Hz
Start
winding
Run
winding
Relay
Note that the relay coil is in
series with the run winding.
When power is applied, the
large current in the relay
coil closes the relay and
applies power to the start
winding. Watch the relay.
14 - <number>

## Slide 26
Relay-Controlled Start Winding
”
”
”
”
Rotor
120 V
60 Hz
Start
winding
Run
winding
Relay
Note that the relay coil is in
series with the run winding.
When power is applied, the
large current in the relay
coil closes the relay and
applies power to the start
winding. Watch the relay.
As the motor builds up
speed, the run current
decreases and the relay
opens the start winding.
14 - <number>

## Slide 27
Reversible Permanent-Split Capacitor Motor
Winding
# 2
Rotor
120 V
60 Hz
The capacitor is in series
with winding # 1. Thus, the
current in this winding will
will lead the current in the
other winding. Rotation is
clockwise.
Watch the switch and direction arrows .
Winding
# 1
(Page 394)
14 - <number>

## Slide 28
Winding
# 2
Rotor
Winding
# 1
120 V
60 Hz
The capacitor is in series
with winding # 1. Thus, the
current in this winding will
will lead the current in the
other winding. Rotation is
clockwise.
Throwing the switch
puts the capacitor in
series with winding #2.
This reverses rotation
because current in
winding #2 is now the
leading current.
Note that the two windings are identical.
Reversible Permanent-Split Capacitor Motor
(Page 394)
14 - <number>

## Slide 29
Two-Value-Capacitor Motor (Page 394)
Start
winding
Rotor
Run
winding
120 V
60 Hz
Run capacitor
Start capacitor
The run capacitor is an
oil-filled, low-value
capacitor that gives the
motor the run character-
istics of the permanent-
spilt capacitor motor.
The start capacitor, being
a high-value, ac electro-
lytic, provides high start-
ing torque when the start
switch is closed by a
centrifugal switch
actuator.
14 - <number>

## Slide 30
Pole
# 1
Pole
# 2
Compound Dc Motor (Page 399)
Each field pole has two windings.
One winding is connected to the dc source.
The other winding is connected in series with the armature.
Armature
This series combination is also connected to the source.
Thus, the compound motor has some of the desirable
characteristics of both series and parallel motors.
14 - <number>

## Slide 31
Other-Motors Quiz
The mechanically-operated start-switch in a
split-phase motor can be replaced with a ____.
relay
The coil of the starting relay is in series with
the ____ winding.
run
The windings in a reversible, permanent-split,
capacitor motor are _____.
identical
The two-value, capacitor motor is a type of
____ _____ capacitor motor.
permanent-split
A dc motor with part of the field-pole winding
in series with the armature is called
a(n) ____ dc motor.
compound
14 - <number>

## Slide 32
Concept Review
Repeat Segment
The relay coil is in the run winding when
the start winding is relay controlled.
In a permanent-split capacitor motor,
the capacitor can be in either winding.
The two-value-capacitor motor has the
desirable characteristics of the capacitor-
start and the permanent-capacitor motors.
The compound dc motor has the desirable
characteristics of the series dc and the
parallel dc motors.
14 - <number>

## Slide 33
REVIEW
Motor Ratings
Parts of a Motor
Rotating Magnetic Fields
Split-Phase Motors
Dc Motors
14 - <number>