## Slide 1
PHOTO GALLERY Study Guide in PowerPoint to accompany Thermodynamics: An Engineering Approach, 8th edition by Yunus A. Çengel and Michael A. Boles

## Slide 2
List Of Slides
3 Heat pump systems
4 Spark ignition internal combustion engine
5 Automobile heater core
6 Cut away of a hair drier
7 Throttle or expansion tube
8 Two-stage, intercooled refrigerant compressor
9 Shell and tube heat exchanger
10 Forced draft cooling tower
11 Honey comb like structure inside forced draft cooling tower
12 Components of a two-stage, air compressor with intercooling
13 Steam turbine blades
14 Compost pile

## Slide 3
A typical heat pump system is shown here. In the heating mode high-pressure vapor refrigerant is sent to the indoor heat exchanger coil. The refrigerant gives up its energy to the inside air and condenses to a high-pressure liquid. The liquid is throttled to a low-pressure, low-temperature liquid-vapor in the outdoor coil and receives energy from the from the outside air. The refrigerant vaporizes, enters the compressor as a low-pressure vapor to be compressed to the high-pressure, and the cycle is completed.
Heat Pump Systems

## Slide 4
Spark ignition internal combustion engine
Photo by M. Boles

## Slide 5
The heat exchanger shown here is typical of liquid-to-gas heat exchangers. In this case hot coolant from a 1966 Mustang engine flows into and out of the heat exchanger through the inlet and exit tubes. Air from the passenger compartment is heated as it flows through the fins.
Photo by M. Boles

## Slide 6
A hair drier is an example of a one entrance, one exit open system that receives electrical work input to drive the fan and power the resistance heater.
Photo by M. Boles

## Slide 7
Throttle or expansion tube.
Throttle may be a simple as the expansion tube used in automobile air conditioning systems to cause the refrigerant pressure drop between the exit of the condenser and the inlet to the evaporator.
Photo by M. Boles

## Slide 8
One stage of a two-stage, intercooled refrigerant compressor in a chilled water refrigeration system
Photo by M. Boles

## Slide 9
Typical shell and tube heat exchanger used for the intercooler, evaporator, and condenser for a chilled water refrigeration system.
Photo by M. Boles

## Slide 10
Forced draft cooling tower for cooling water used in the intercooler and condenser heat exchangers of the chilled water refrigeration system
Photo by M. Boles

## Slide 11
Honey comb like structure inside forced draft cooling tower to cause better mixing of the cooling water and air.
Photo by M. Boles

## Slide 12
Another application of intercooling to reduce compressor work is shown here as a two-stage, 7.5 hp air compressor with intercooling attached to an eighty gallon tank.
First stage piston with second stage piston in back
Intercooling heat exchanger
Drive wheel spokes function as fan blades
Photo by M. Boles

## Slide 13
High pressure steam turbine blade.
Length is approximately 20 cm (8 in.).
Low pressure steam turbine blade.
Length is approximately 70 cm (30 in.).
Steam turbine blades
Photos by M. Boles

## Slide 14
Compost pile
The chemical reaction in the compost pile shown below is an example of an exothermic reaction. On the day this photo was taken, the ambient temperature was 69°F. At two feet inside the pile, the temperature was 135°F.
Photo by M. Boles