## Slide 1: Tippens Physics 7th Edition Chapter 13
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 2: Question 1
A material having a large spring constant will experience a greater change in length for a given applied force than a material with a small spring constant.
A. True
B. False

## Slide 3: Question 2
Stress is the relative change in the dimensions or shape of a body as the result of an applied force.
A. True
B. False

## Slide 4: Question 3
The ultimate strength of a material is the greatest stress it can withstand without rupturing.
A. True
B. False

## Slide 5: Question 4
The smaller the bulk modulus of a material, the higher its compressibility.
A. True
B. False

## Slide 6: Question 5
The radian may be a unit of strain.
A. True
B. False

## Slide 7: Question 6
The modulus of elasticity has the same units as stress.
A. True
B. False

## Slide 8: Question 7
Young's modulus is constant for a particular material but varies with the length and cross-sectional area of a wire.
A. True
B. False

## Slide 9: Question 8
Water has a greater compressibility than steel.
A. True
B. False

## Slide 10: Question 9
Usually the shearing strain can be approximated by the tangent of the shearing angle.
A. True
B. False

## Slide 11: Question 10
Young's modulus applies for compressive stresses as well as tensile stresses.
A. True
B. False

## Slide 12: Question 11
A shearing stress acting on a body changes its
A. shape.
B. volume.
C. length.
D. area.

## Slide 13: Question 12
A unit for strain is the
A. inch.
B. pound per square inch.
C. newton per centimeter.
D. radian.

## Slide 14: Question 13
The volume strain for a constant applied force increases directly with an increase in
A. surface area.
B. compressibility.
C. volume.
D. bulk modulus.

## Slide 15: Question 14
The modulus of rigidity is another name for
A. compressibility.
B. bulk modulus.
C. shear modulus.
D. Young's modulus.

## Slide 16: Question 15
When a force of 20 N produces an elongation of 0.4 cm, the spring constant is
A. 5 N/cm.
B. 50 N/cm.
C. 8 N * cm.
D. 0.02 cm/N.

## Slide 17: Question 16
The cross-sectional area of a 20-in. copper wire is 0.001 in. A force of 400 lb causes a stress of
A. 4 x 10^5 lb/in.
B. 0.4 lb/in.
C. 20 lb/in.
D. 50 lb/in.

## Slide 18: Answer Key
1. B
2. B
3. A
4. A
5. A
6. A
7. B
8. A
9. A
10. A
11. A
12. D
13. B
14. B
15. B
16. A