## Slide 1: Tippens Physics 7th Edition Chapter 30
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 2: Question 1
The sensitivity of a galvanometer is determined entirely by its electric resistance.
A. True
B. False

## Slide 3: Question 2
A horizontal current loop that is parallel with a magnetic field directed from right to left will experience a counterclockwise torque if the loop current is counterclockwise when viewed from the top.
A. True
B. False

## Slide 4: Question 3
The radial magnetic field for galvanometer helps to ensure that the pointer deflection will be directly proportional to the current in the coil.
A. True
B. False

## Slide 5: Question 4
Placing a low-resistance wire across the terminals of an ammeter will decrease the range of currents that can be measured.
A. True
B. False

## Slide 6: Question 5
Increasing the multiplier resistance for a voltmeter will increase the range of the voltmeter.
A. True
B. False

## Slide 7: Question 6
Voltmeters must be connected in parallel because of the low multiplier resistance that would short-circuit the circuit if it were placed in series.
A. True
B. False

## Slide 8: Question 7
The proper insertion of an ammeter or a voltmeter into a circuit will alter the current in that circuit slightly, introducing some error.
A. True
B. False

## Slide 9: Question 8
The torque output by a simple dc motor is not uniform.
A. True
B. False

## Slide 10: Question 9
Which of the following must be a high-resistance instrument?
A. Voltmeter
B. Ammeter
C. Motor
D. Galvanometer

## Slide 11: Question 10
The minimum range of a given ammeter is determined by the
A. value of the shunt resistance.
B. value of the multiplier resistance.
C. load resistance.
D. resistance and spring tension in the galvanometer element.

## Slide 12: Question 11
The range of a dc voltmeter can be increased by
A. increasing the circuit load resistance.
B. increasing the multiplier resistance.
C. decreasing the multiplier resistance.
D. placing a shunt resistance across the voltmeter terminals.

## Slide 13: Answer Key
1. B
2. A
3. A
4. B
5. A
6. B
7. A
8. A
9. A
10. D
11. B