## Slide 1: Tippens Physics 7th Edition Chapter 31
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 2: Question 1
Lenz's law is a consequence of the fact that energy must be conserved.
A. True
B. False

## Slide 3: Question 2
The magnitude of an induced emf is directly proportional to the rate at which magnetic flux lines are cut by a conductor.
A. True
B. False

## Slide 4: Question 3
A generator is a device that converts magnetic energy to electric energy.
A. True
B. False

## Slide 5: Question 4
A transformer can be used for alternating current only.
A. True
B. False

## Slide 6: Question 5
The back emf in the armature of an electric motor is zero when the motor is started and rises as the motor's speed increases.
A. True
B. False

## Slide 7: Question 6
If the armature of a generator is rotating with a constant angular velocity in a constant magnetic field, the induced emf will be constant.
A. True
B. False

## Slide 8: Question 7
For an ac generator, the maximum current occurs when the induced emf is a minimum.
A. True
B. False

## Slide 9: Question 8
Every motor is also a generator.
A. True
B. False

## Slide 10: Question 9
In a shunt-wound motor, the output speed can be controlled by varying the input current to either the field windings or the armature windings.
A. True
B. False

## Slide 11: Question 10
A series-wound motor is preferable if a large starting torque is desirable.
A. True
B. False

## Slide 12: Question 11
A wire parallel to the paper moves downward into a flux density directed into the paper. The induced current will be
A. directed to the left.
B. zero because the motion is perpendicular to the field.
C. directed to the right.
D. opposite to the induced emf, according to Lenz's law.

## Slide 13: Question 12
The instantaneous emf produced by a simple ac generator is a maximum when the angular displacement of the loop is an
A. integral multiple of p/2.
B. odd multiple of p/2.
C. even multiple of p.
D. odd multiple of p.

## Slide 14: Question 13
A transformer has 400 secondary turns and only 50 primary turns. If an ac voltage of 120 V is connected to the primary coil, the output voltage is
A. 15 V.
B. 240 V.
C. 430 V.
D. 960 V.

## Slide 15: Answer Key
1. A
2. A
3. B
4. A
5. A
6. B
7. B
8. A
9. A
10. A
11. C
12. B
13. D