## Slide 1: Tippens Physics 7th Edition Chapter 32
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 2: Question 1
In a capacitive circuit, the current delivered to a capacitor will rise to 63 percent of its maximum value after charging for a period of one time constant.
A. True
B. False

## Slide 3: Question 2
In an inductive circuit, the current decays to 37 percent of its initial value in a period of one time constant.
A. True
B. False

## Slide 4: Question 3
A capacitor with a breakdown voltage of 150 V would be safe to use in an ac circuit if the ac voltage were only 120 V.
A. True
B. False

## Slide 5: Question 4
Capacitive reactance and inductive reactance increase with an increase in frequency of an alternating current.
A. True
B. False

## Slide 6: Question 5
The power factor in an ac circuit is the ratio of its resistance to its impedance.
A. True
B. False

## Slide 7: Question 6
Under a condition of resonance in an ac circuit, the current will be in phase with the voltage.
A. True
B. False

## Slide 8: Question 7
Reactance, impedance, and resistance are all measured in the same physical unit (ohms).
A. True
B. False

## Slide 9: Question 8
A negative phase angle occurs when the current leads the voltage in an ac circuit.
A. True
B. False

## Slide 10: Question 9
An alternating voltage has a maximum value of 30 V. The effective value is approximately
A. 15 V
B. 21.2 V
C. 30 V
D. 42.9 V

## Slide 11: Question 10
As the capacitance in an ac circuit increases, the resonant frequency
A. increases
B. decreases
C. remains the same
D. approaches zero

## Slide 12: Question 11
The ratio of the pure resistance in an ac circuit to the impedance is known as the
A. power factor
B. phase angle
C. resonant frequency
D. net reactance

## Slide 13: Question 12
In a circuit containing pure capacitance, during a period of one time constant, the
A. charge decays to 63 percent of its initial value
B. charge increases to 37 percent of its initial value
C. current decays to 37 percent of its initial value
D. capacitor is completely charged

## Slide 14: Question 13
In an ac circuit containing a coil with an inductance of 0.3 H, the voltage is 120 V at 60 Hz. If we neglect resistance, the effective current in the coil is
A. 0.27 A
B. 0.53 A
C. 1.06 A
D. 2.12 A

## Slide 15: Question 14
A circuit contains a 12-degree F capacitor, a 40-ohm resistor, a switch, and a 20-V dc battery connected in series. After the switch is closed, the capacitor can be considered fully charged after
A. 0.00048 s
B. 0.0012 s
C. 0.0024 s
D. 0.0048 s

## Slide 16: Answer Key
1. B
2. A
3. B
4. B
5. A
6. A
7. A
8. A
9. B
10. B
11. A
12. C
13. C
14. C