## Slide 1: Tippens Physics 7th Edition Chapter 27
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 2: Question 1
The electromotive force is a force exerted on an electric charge to keep it moving.
A. True
B. False

## Slide 3: Question 2
The direction of conventional current for a conductor is opposite to the direction of electron flow.
A. True
B. False

## Slide 4: Question 3
Electric current is also a measure of the average speed with which electrons move in a conductor.
A. True
B. False

## Slide 5: Question 4
According to Ohm's law, the electric current is inversely proportional to the applied voltage.
A. True
B. False

## Slide 6: Question 5
Electric resistance increases with an increase in the cross-sectional area of a conductor.
A. True
B. False

## Slide 7: Question 6
The resistivity of a wire is independent of the length of the wire.
A. True
B. False

## Slide 8: Question 7
A wire with a diameter of 0.002 in. has a cross-sectional area of 4 cmils.
A. True
B. False

## Slide 9: Question 8
The temperature coefficient of resistance is equal to the change in resistance per degree change in temperature.
A. True
B. False

## Slide 10: Question 9
The power loss in a wire is quadrupled if the current is doubled.
A. True
B. False

## Slide 11: Question 10
A rheostat is a meter that indicates the electric resistance in a circuit.
A. True
B. False

## Slide 12: Question 11
A unit of electromotive force is the
A. joule.
B. newton.
C. volt.
D. watt.

## Slide 13: Question 12
If one were to use a water analogy to study electric current, voltage would be most similar to
A. force.
B. pressure.
C. rate of flow.
D. density.

## Slide 14: Question 13
The potential difference between the terminals of a small heater is 60 V. If the resistance of the heater is 30 O, the current is
A. 0.5 A.
B. 2 A.
C. 1800 A.
D. 3 A.

## Slide 15: Question 14
A 120-V heater has a resistance of 600 O. The heat energy generated in 1 min is
A. 24 J.
B. 120 J.
C. 1200 J.
D. 1440 J.

## Slide 16: Answer Key
1. B
2. A
3. B
4. B
5. B
6. A
7. A
8. B
9. A
10. B
11. C
12. B
13. B
14. D