## Slide 1: Tippens Physics 7th Edition Chapter 28
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 2: Question 1
The rules for computing equivalent resistance are the same as those for computing equivalent capacitance.
A. True
B. False

## Slide 3: Question 2
The current is the same in all parts of a parallel circuit.
A. True
B. False

## Slide 4: Question 3
The equivalent resistance of two resistors in parallel is equal to their product divided by their sum.
A. True
B. False

## Slide 5: Question 4
The emf is essentially equal to the open-circuit potential difference.
A. True
B. False

## Slide 6: Question 5
The current supplied to an electric circuit is equal to the net emf divided by the total resistance of the circuit if we neglect internal resistance.
A. True
B. False

## Slide 7: Question 6
Kirchhoff's second law applies for each current loop in a complex circuit and not just for the total circuit.
A. True
B. False

## Slide 8: Question 7
In applying Kirchhoff's laws, the tracing direction must be the same as the current direction.
A. True
B. False

## Slide 9: Question 8
When the Wheatstone bridge is balanced, the voltage between the galvanometer and either terminal of the source of emf will be the same.
A. True
B. False

## Slide 10: Question 9
Kirchhoff's laws apply only for current loops that contain at least one source of emf.
A. True
B. False

## Slide 11: Question 10
When two identical resistors are connected in parallel, the voltage drop across each is one-half of the terminal potential difference at the source of emf.
A. True
B. False

## Slide 12: Question 11
The variance of terminal potential difference, as compared with emf, is due to
A. the circuit load.
B. the internal resistance.
C. Kirchhoff's law.
D. current delivered.

## Slide 13: Question 12
When using the Wheatstone bridge, the quantity that is balanced is
A. voltage.
B. resistance.
C. current.
D. emf.

## Slide 14: Answer Key
1. B
2. B
3. A
4. A
5. B
6. A
7. B
8. A
9. B
10. B
11. B
12. A