## Slide 1: Tippens Physics 7th Edition Chapter 12
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 2: Question 1
The efficiency of a machine is defined as the ratio of the work input to the work output.
A. True
B. False

## Slide 3: Question 2
The actual mechanical advantage of a machine can never be less than unity.
A. True
B. False

## Slide 4: Question 3
The wheel and axle is an application of the principle of the lever.
A. True
B. False

## Slide 5: Question 4
A single fixed pulley offers no mechanical advantage; it changes only the direction of an input force.
A. True
B. False

## Slide 6: Question 5
In a pulley system with a speed ratio greater than 1, the output torque is less than the input torque.
A. True
B. False

## Slide 7: Question 6
In a machine using two gears in which the number of teeth on the input gear is greater than the number of teeth on the output gear, there will be a reduction in the output torque.
A. True
B. False

## Slide 8: Question 7
In a belt drive, maximum efficiency is obtained for minimum belt tension.
A. True
B. False

## Slide 9: Question 8
For an inclined plane, the actual mechanical advantage is the ratio of the slope distance to the height of the plane.
A. True
B. False

## Slide 10: Question 9
For a screw jack, a larger pitch results in a smaller mechanical advantage.
A. True
B. False

## Slide 11: Question 10
Which of the following machines is not an application of the lever principle?
A. Screw jack
B. Wheelbarrow
C. Wheel and axle
D. Pliers

## Slide 12: Question 11
An 80-hp motor has an efficiency of 60 percent. The output power is approximately
A. 133 hp.
B. 75 hp.
C. 60 hp.
D. 48 hp.

## Slide 13: Question 12
An iron pipe 10 ft long is used to lift a 400-lb weight. If the fulcrum is placed 2 ft from the weight, the force that must be exerted at the end of the pipe is approximately
A. 200 lb.
B. 100 lb.
C. 40 lb.
D. 80 lb.

## Slide 14: Question 13
The ideal mechanical advantage of a belt drive is 4.0. If the angular speed of the input pulley is 8 rad/s, the angular speed of the output pulley is
A. 2 rad/s.
B. 32 rad/s.
C. 0.5 rad/s.
D. 4 rad/s.

## Slide 15: Question 14
A 100-lb box is pushed up a 200-ft ramp to a height of 20 ft. The ideal mechanical advantage is approximately
A. 4.
B. 10.
C. 5.
D. 0.1.

## Slide 16: Question 15
Consider a belt drive in which the diameter of the driving pulley is 8 cm and the diameter of the driven pulley is 24 cm. If the efficiency is 50 percent, what is the actual mechanical advantage?
A. 15
B. 6
C. 1.5
D. 3

## Slide 17: Question 16
In the operation of a screw jack of pitch 0.1 in., the input force of 4 lb turns through a circle of radius 2 ft, lifting an 80-lb weight. The efficiency is approximately
A. 48 percent.
B. 14.4 percent.
C. 20 percent.
D. 1.3 percent.

## Slide 18: Answer Key
1. B
2. B
3. A
4. A
5. B
6. A
7. A
8. B
9. A
10. A
11. D
12. B
13. A
14. B
15. C
16. D