## Slide 1: Tippens Physics 7th Edition Chapter 20
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 2: Question 1
In the absence of friction, heat engines are 100 percent efficient.
A. True
B. False

## Slide 3: Question 2
If the first law of thermodynamics is satisfied, the second law will also be satisfied.
A. True
B. False

## Slide 4: Question 3
In every thermodynamic process, the heat absorbed by a system must equal the sum of the work done by the system and its change in internal energy.
A. True
B. False

## Slide 5: Question 4
During an isothermal expansion, all the absorbed thermal energy is converted to useful work.
A. True
B. False

## Slide 6: Question 5
All Carnot engines are perfect engines and, therefore, operate at 100 percent efficiency.
A. True
B. False

## Slide 7: Question 6
The greater the difference between the input and output temperatures of a steam engine, the greater the efficiency of the engine.
A. True
B. False

## Slide 8: Question 7
A high compression ratio of an internal combustion engine means a higher operating efficiency.
A. True
B. False

## Slide 9: Question 8
The coefficient of performance for a refrigerator is a measure of cooling efficiency and is expressed as a percentage.
A. True
B. False

## Slide 10: Question 9
The thermodynamic state of a gas refers to
A. its pressure.
B. its volume.
C. its temperature.
D. all of these.

## Slide 11: Question 10
An engine that operates with 100 percent efficiency
A. is a Carnot engine.
B. violates the first law.
C. has an Otto cycle.
D. violates the second law.

## Slide 12: Question 11
If a heat engine absorbs heat at 600 K and rejects heat at 200 K, its efficiency is
A. 33 percent.
B. 50 percent.
C. 67 percent.
D. 80 percent.

## Slide 13: Question 12
In a Carnot cycle, 1600 cal is absorbed at 600 K, and 400 cal is exhausted to a cold reservoir. The temperature of the cold reservoir is
A. 150 K.
B. 200 K.
C. 450 K.
D. 800 K.

## Slide 14: Question 13
An adiabatic process is one in which
A. the temperature is constant.
B. the pressure is constant.
C. the volume is constant.
D. no heat enters or leaves the system.

## Slide 15: Question 14
If the adiabatic constant is 1.4 and the compression ratio is 6, a gasoline engine has an efficiency of
A. 45 percent.
B. 51 percent.
C. 56 percent.
D. 64 percent.

## Slide 16: Question 15
In a typical refrigerator, heat is extracted from the interior by the
A. compressor.
B. evaporator.
C. condenser.
D. throttling valve.

## Slide 17: Answer Key
1. B
2. B
3. A
4. A
5. B
6. A
7. A
8. B
9. D
10. D
11. C
12. A
13. D
14. B
15. B